## Slide 1: Advanced Robotics Programming Class Lesson 9: Advanced Robot Navigation
Titan Robotics Club FRC492
Michael Tsang (Programming Mentor)

## Slide 2: Agenda
In this lesson, you will learn:
  Passive-wheel Odometry
  Sensor Drive
  Vision Drive
  Pure Pursuit Drive

## Slide 3: Passive-wheel Odometry
The drive bases (simple, mecanum, swerve) created by the TRC library has built-in odometry that uses the encoders of the wheel motors and a gyro. The built-in odometry works fine as long as the wheels don’t slip.
If any of the driving wheels slipped or the robot hits the wall or being hit by another robot, the robot displacement may not be registered by the built-in odometry. This means the odometry is no longer accurate.
One solution to this problem is to use external passive-wheel odometry. A passive-wheel odometry sensor is built with passive omni-wheels with an encoder. It has no motor but if the wheel turns, the encoder will register rotation. If we put two passive-wheel odometry sensors one for each axis and spring loaded them to the ground, they will keep track of movements on both axes accurately even if the robot wheels slipped or the robot being pushed by other robots.

## Slide 4: TrcDriveBaseOdometry Class
TrcDriveBaseOdometry class provides external odometry device support for the drive base. It supports 5 different configurations:
  2-sensor configuration: one Y-axis encoder sensor and one gyro rotation sensor.
  3-sensor configuration 1: one X-axis encoder sensor, one Y-axis encoder sensor and one gyro rotation sensor.
  3-sensor configuration 2: two Y-axis encoder sensors and one gyro rotation sensor.
  4-sensor configuration: one X-axis encoder sensor, two Y-axis encoder sensors and one gyro rotation sensor.
  5-sensor configuration: two X-axis encoder sensor, two Y-axis encoder sensors and one gyro rotation sensor.
X/Y axis encoders must be installed parallel to the respective axis and tangential to the centroid of the drive base.
X/Y axis encoders can be installed with an offset from the centroid of the drive base.
For X-axis, the offset of the front sensor must be zero or positive, the offset of the back sensor must be zero or negative.
For Y-axis, the offset of the left sensor must be zero or positive, the offset of the right sensor must be zero or negative.

## Slide 5: TrcDriveBaseOdometry Class (continue)
TrcDriveBaseOdometry Constructor: array of X-axis sensors, array of Y-axis sensors, rotation sensor.
Methods:
  setOdometryScales – set X, Y and rotation scale factors (scaling sensor units into real world units).
  resetOdometry – reset odometry with options to reset the sensor hardware and rotation sensor.
  getOdometryDelta – reads all sensors and calculate the delta displacements of all axes from the last odometry update, called periodically by the drive base class to integrate delta displacements into absolute field position.

## Slide 6: Sensor Drive
A drive base has a number of degrees of freedom. A tank drive base has 2: Y-axis and rotation. A mecanum or swerve drive base has 3: X-axis, Y-axis and rotation.
In order to navigate a drive base, there must be a number of controllers equal to the number of degrees of freedom. TRC Library provided a generic PID controlled drive class (TrcPidDrive.java) that can PID controlled drive up to 3 degrees of freedom. Therefore, it takes up to 3 PID controllers, one for each degree of freedom: X-PID controller, Y-PID controller and Turn-PID controller.
Each PID controller must be able to get feedback on the movement along its degree of freedom. Typically, for X and Y axes, we use encoders to tell us how far the robot has moved in the corresponding axes. For rotation, we use gyro to tell us the robot’s heading. These are feedback sensors.
One could be creative on using different sensors to achieve different PID controlled drive scenarios. For example, using ultrasonic sensor as the Y-axis feedback sensor allows the robot to drive up to a given distance from an obstacle. Using a pair of distance sensors on the side of the robot as turn feedback sensors allows the robot to follow the wall. Using one or more light sensors pointing to the ground as rotation feedback sensors allows the robot to follow a line on the ground. Camera and vision processing can detect the distance and angle of your target. Using distance info as the Y-axis feedback sensor and angle info as rotation feedback sensor allows the robot to navigate and align to the target.

## Slide 7: PID Control Drive Using Sensors
TrcPidDrive provides different drive options:
  setRelativeTarget – Typically uses encoders as X/Y feedback sensors and gyro as heading sensor. Targets are set as relative distance from current position.
  setAbsoluteTarget – Typically uses encoders as X/Y feedback sensors and gyro as heading sensor. Targets are absolute field position.
  setSensorTarget – All three degrees of freedom can use any type of sensors. The target values are generally absolute sensor values. For example, using ultrasonic sensor to drive the robot to N inches in front of an obstacle, the Y target will be set as absolute N inches. Using light sensor to follow a line on the floor will set the turn target value as the absolute light value average between the white line and the dark floor. Sometimes it is useful for a PID controller to use multiple sensors to control a degree of freedom. For example, using a pair of distance sensors to control the turn target can be used to follow the wall. Just set the absolute turn target to zero and report the heading to the PID controller by subtracting the back distance sensor from the front distance sensor. Note that AbsoluteTargetMode cannot be used in setSensorTarget.

## Slide 8: Exercise: Wall Following Drive
Strafe the robot to the side wall until it is 12 inches away from it. Use two distance sensors to drive the robot following the wall for 10 feet.
  Create two distance sensor objects such as the FrcLaserShark.
  Create a mecanum drive base.
  Create three PID controllers:
    X PID controller averages the two distance sensors to control the X distance from the wall.
    Y PID controller uses the drive base encoders to control the Y distance to travel.
    Turn PID controller uses the difference of the distance sensors to control the heading of the robot.
  Create a PID drive using the three PID controllers.
  Create an autonomous command module which implements a state machine to:
    Strafe sideways until the robot is 12 inches away from the wall.
    Go forward 10 feet and maintaining the distance of 12 inches from the wall.
    Stop.
  Add the autonomous command module as one of the autonomous choices.

## Slide 9: What Is Vision Processing?
Using camera allows the robot to see things but seeing things means more than just capturing a picture. A picture is not very useful unless it is “interpreter” or “processed” by somebody to figure out what objects are in the picture and where they are relative to the camera.
Fortunately, there are object detection libraries such as OpenCV (Open Source Computer Vision). They can do vision processing on a picture and return useful info such as object types detected and object locations. Some libraries even provide “Machine Learning” tools that allow you to feed thousands of pictures to it so it can learn different type of objects. These are very advanced topics that we don’t have to deal with. In other words, they are generally provided to us in the form of library APIs or even camera firmware.
What we are discussing here is how to use the processed vision info to navigate the robot.

## Slide 10: Vision Info Processing
Generally, for each picture frame it processed, vision returns an array of objects with the following info:
  The type of object detected.
  The rectangle of the detected object (includes the pixel coordinates of the center of the detected object and the size of the detected object).
  Some vision processor may include confidence level.
Our processing:
  Apply filtering algorithm to eliminate false detection and hopefully we will have exactly one object in the array which is our target.
  If the array still contains more than one object, the objects in the array should be sorted with highest confidence first so we will just pick the first object on the list.
  Translate the pixel coordinates and size into real world units (TrcHomographyMapper). This includes the distance of the object from the robot and the angle alignment of the object relative to the robot’s heading.
With the object distance and angle info, one can create a PID controlled drive (TrcPidDrive) using the vision info of the detected object to control the Y axis travel and robot heading.

## Slide 11: What Is Pure Pursuit Drive?
In autonomous, we usually program the robot to drive to a location using PID controlled drive doing multiple segments, one degree of freedom at a time. Each segment of PID drive involves the robot accelerating at the beginning and decelerating at the end. Sometimes going back and forth to achieve target within tolerance before moving on to the next segment. This wastes a lot of precious autonomous time.
Pure Pursuit Drive solves this problem by navigating the robot following a given path smoothly. Since it is a single path, there is no intermediate segment for which the robot would stop at the end of each segment.
Pure Pursuit path is defined by a set of waypoints. Pure Pursuit will interpolate a smooth curve passing through each waypoint in the path and will try to follow the path to the final destination in one smooth movement.
Abhay did a good job implementing Pure Pursuit Drive in our library. He also created a great document explaining Pure Pursuit Drive and among other things in robotics: FRC Guidebook.docx - Microsoft Word Online (live.com).

## Slide 12: Using Pure Pursuit Drive
TrcHolonomicPurePursuitDrive Constructor: instance name, drive base, following distance, position tolerance, turn tolerance, position control PID coefficients, turn control PID coefficients, velocity control PID coefficients.
Methods:
  Some setter methods to set various parameters of Pure Pursuit Drive: e.g. following distance, tolerances, PID coefficients, interpolation types etc.
  isActive – check if Pure Pursuit Drive is in progress.
  cancel – cancel the Pure Pursuit Drive that is in progress.
  start – start the pure pursuit drive with the specified path. void start(TrcPath path, TrcEvent onFinishedEvent, double timeout);

## Slide 13: TrcPath
TrcPath defines a path for the robot to follow and whether waypoint headings are in degrees or radians. A path is an array of waypoints.
A waypoint defines a point on the path and contains info such as:
  timestep – a timestamp relative to the starting time of the path. This is optional and is only required for a certain motion drive strategies (not needed by Pure Pursuit).
  pose – location of the waypoint: X, Y and heading. This is always required for any motion drive strategies.
  encoderPosition – specifies the encoder position at this waypoint (not needed by Pure Pursuit).
  velocity – specifies the tangential velocity of the robot at this waypoint (not needed by Pure Pursuit).
  acceleration – specifies the tangential acceleration of the robot at this waypoint (not needed by Pure Pursuit).
  jerk – specifies the jerk (derivative of acceleration) of the robot at this waypoint (not needed by Pure Pursuit).
There are two types of path:
  Absolute path: the location of each waypoint is an absolute position in a reference frame (usually the competition field).
  Incremental path: the location of each waypoint is a relative position from the previous waypoint on the path.

## Slide 14: TrcPathBuilder
TrcPathBuilder is a utility class that makes it easier to build paths for Pure Pursuit Drive.
Pure Pursuit Drive requires an absolute path but relative to the first waypoint in the path.
TrcPathBuilder can build such a path for Pure Pursuit from a field absolute path or an incremental path.
TrcPathBuilder Constructor:
  startingPose – absolution position of the robot at the start of the path (i.e. absolute field position of the robot).
  incrementalPath – specifies whether the path is given as incremental path or absolute path.
  inDegrees – specifies whether the waypoint headings are in degrees or radians.
Methods:
  append – append a point to the path (the point can be a waypoint or a pose).
  toPath – returns a path that contains absolute waypoints in the reference frame.
  toRelativeStartPath – returns a path that contains waypoints relative to the first waypoint of the path (this is the type of path Pure Pursuit needs).

## Slide 15: Exercise: Drive Robot Through a Slalom Path
Navigate the robot through a slalom path using Pure Pursuit Drive.
  Create a mecanum drive base.
  Set the initial robot position to the field position of (x=72.0, y=9.0, angle=0.0). Hint: driveBase.setFieldPosition(…)
  Create a TrcHolonomicPurePursuitDrive obect with: 6-inch followingDistance, 3-inch positionTolerance, 2-degree turn Tolerance and three sets of PID coefficients (position, turn and velocity).
  Create a CmdSlalomDrive command module.
  In the command module, use TrcPathBuilder to create a path for an incremental slalom course with the following 9 relative points:
    (0, 27, -90), (0, 24, 90), (0, 24, 90), (0, 48, -90), (0, 24, -90), (0, 48, 90), (0, 24, 90), (0, 24, -90), (0, 24, 0)
  Create a state machine that contains the following states:
    PURE_PURSUIT_DRIVE: execute Pure Pursuit Drive with the path from above.
    DONE: stop.
  Add the autonomous command module as one of the autonomous choices.