## Slide 1: Advanced Robotics Programming Class Lesson 2: Basic Robot Components
Titan Robotics Club FRC492
Michael Tsang (Programming Mentor)

## Slide 2: Agenda
In this lesson, you will learn:
  Information Displays
    Java Console
    Dashboard: Shuffleboard
  Game Controller and Button Panel
  Motor Controllers
  Servo Motors
  Relays
  Pneumatics
  Sensors
  Indicators

## Slide 3: Information Display
For operating the robot and for debugging, we need mechanisms to display information from your code to the Driver Station Laptop. There are two main display mechanisms:
  Java Console: mainly for outputting information as strings and will scroll away as more information is printed to the console.
  Dashboard: can be bidirectional, outputting as well as inputting information. Information can be of different data types (Boolean, Number, String, Raw date bytes).
    Output: Can select how the info is displayed. If displayed as text/number fields, they are displayed at fixed locations on the screen, will not scroll away but will keep changing as the information is updated. If desire to see history of the changing values, one can display the values as a time graph.
    Input: Allows user to input information (Boolean, Number, String, SendableChooser) so that robot code can read them. Example uses include picking autonomous strategies and competition parameters.

## Slide 4: Java Console
Standard console associated with the Java VM. Can be written to by calling System.out methods such as println(), print() and printf() to output strings. Java Console can be hosted by Visual Studio Code or Driver Station app. This tends to be quite chatty because all code components write to it, including our code, WPILib, 3rd-party Vendor Libraries and other systems. Outputs are also captured into the RoboRIO log file for post examination.
Pros:
  Captures everything in chronological order (i.e. what happens before what).
  Keeps history of the values if data is printed periodically so you can examine the data trend.
Cons:
  Captures everything and thus quite chatty. Information could be hard to spot especially if information are printed periodically at a fast rate.
  If information is printed periodically, it could overwhelm the console (hundreds of lines per second). Console usually has a limited buffer capacity which means you will start losing info at the beginning when the buffer gets full.

## Slide 5: Console Output: TrcDbgTrace
Provided by our framework and is built on top of console output.
Features additional to conventional console output:
  Allows specifying different message level of the output information thus allowing verbosity filtering (traceFatal, traceErr, traceWarn, traceInfo, traceVerbose).
  Allows logging to our own log file asynchronously thus filtering out information from other parties (reducing chatters).
  Provides methods to print the thread stack (printThreadStack) giving you the ability to “catch the culprit” during debugging (i.e. who did this?).
  Provides methods to log events. Unlike messages that are unstructured, events are structured output that can be parsed by analytic tools such as TrcTraceLogAnalyzer that can visually replay events occurred in autonomous, for example.
Get an instance of TrcDbgTrace: TrcDbgTrace.getGlobalTracer() or simply robot.globalTracer.
Useful methods: void traceInfo(String funcName, String format, Object... args) void printThreadStack()
Format String: most commonly used substitutions are %d (for decimal integers), %x (for hexadecimal integers), %f (for floats and doubles) and %s (for strings). For %f, you can even specify decimal places (e.g. %6.3f). For more info about format string, read documentation here.

## Slide 6: Exercise: Console Output
In FrcTeleOp.java, add code in the periodic method to print to the console the square root values of 1 to 100. Useful methods are:
  robot.globalTracer.traceInfo
  Math.sqrt

## Slide 7: Dashboard: FrcDashboard
Dashboard is a plug-in to the Driver Station app. FIRST provided a few Dashboard apps but we will focus on the Shuffleboard app which is what we use. Information is written by calling SmartDashboard methods which communicates with the Shuffleboard app via Network Table. Information written can be of different data types: Boolean, Number, String and Raw data bytes.
Pros:
  Information is updated in a field on the SmartDashboard that won’t scroll away.
  Information can be displayed in different UI: number, text, switch state, or even a time graph or other widgets.
  Dashboard is bidirectional so it can be used to get user input (e.g. making choices for autonomous, or getting input for tuning PID).
Cons:
  Information is always updated to the current value which means you don’t see the value history unless it is displayed in a time graph.
  Will not show time relationship between different data values (e.g. what changed before what?).
  Periodic values will keep changing and will not freeze so you can’t look for a particular value in time.
FrcDashboard is provided by our framework and is built on top of WPILib SmartDashboard.
Features additional to WPILib SmartDashboard:
  Simulates a 16-line LCD display where code can put information in a specified line on the simulated LCD display.
Get an instance of the Dashboard: FrcDashboard.getInstance(), or simply robot.dashboard.
Useful methods: void displayPrintf(int lineNum, String format, Object... args)

## Slide 8: Exercise: Dashboard Output
In FrcTeleOp.java, add code in the periodic method to print the TeleOp running match time on the dashboard. Useful methods are:
  robot.dashboard.displayPrintf
  TrcTimer.getModeElapsedTime or use elapsedTime parameter in the periodic method.

## Slide 9: Game Controllers
Our framework supports the following game controllers
  FrcJoystick: Generic joystick and generic button/switch panels.
  FrcXboxController: Xbox game controller and generic gamepad.
Typical game controller consists of:
  A number of analog sticks (can have multiple axes X/Y).
  A number of analog throttles/twists/triggers.
  A number of buttons.
Button/Switch panel consists of an array of buttons/switches. It is presented as a joystick but with only buttons or switches, no analog control.

## Slide 10: Game Controller: Analog Control
Multi-axes stick: typically X and Y but some support a third axis (e.g. twist).
An axis gives a range of -1.0 to 1.0 with the center at zero, perfect for controlling motors (i.e. axis value can be used to set motor power).
Analog stick returns to center position when released but not necessarily give you zero value causing the robot to drift slowly.
Deadband: a small range of movement near the center of the analog stick is still considered center and thus returns zero value.
Analog control response curve: squared input gives you precise control at the low-end and accelerated control at the high-end.
Y inversion: Joystick was designed for airplane, push away from you is down, giving negative values. But for driving robot, push away from you is forward and need to be positive and therefore must be inverted.
Constructors: FrcJoystick(String instanceName, int controllerNum) FrcXboxController(String instanceName, int controllerNum)
Useful methods: void setYInverted(boolean inverted) double getXWithDeadband(boolean squared) double getTwistWithDeadband(boolean squared)
Chart: Power Output vs Joystick Input

## Slide 11: Exercise: Analog Control
In FrcTeleOp.java, add code in the periodic method to print the X and Y values of an Xbox controller stick to the dashboard. Useful methods are:
  robot.dashboard.displayPrintf
  robot.driverController.getLeftXWithDeadband
  robot.driverController.getRightYWithDeadband
  robot.driverController.getLeftTriggerWithDeadband
Extra credits: get the values of both the left and right triggers, combine them to give you a value range of -1.0 to 1.0 (i.e. pressing left trigger all the way gives you a value of -1 and pressing right trigger all the way gives you a value of 1). Print the combined value on the dashboard.

## Slide 12: Game Controller: Digital Control
Digital controls are buttons and switches that give you two states: ON or OFF (pressed or released).
Our framework library detects edge events of these buttons and switches. It does callbacks on the events. It means it will call your eventHandler method when a press or release event is detected.
Registering a Callback Event Handler for a game controller: robot.driverController.setButtonHandler(this::driverControllerButtonEvent)
Unregistering a Callback Event Handler for a game controller: robot.driverController.setButtonHandler(null)
Callback Event Handler: void driverControllerButtonEvent(int button, boolean pressed)
Three strategies using digital controls:
  Action on pressed.
  Action on toggle.
  Action on pressed and hold, different action on released.

## Slide 13: Exercise: Digital Control
In FrcTeleOp.java, add code to the buttonEvent handler of the game controller (driverControllerButtonEvent) to print a message when a button on the game controller is pressed or released on the dashboard. Useful methods are:
  robot.dashboard.displayPrintf
  robot.driveController.setButtonHandler
Extra credits: create a boolean variable and use the three different digital control strategies to set its state. Print a message to the dashboard showing the state of the variable.

## Slide 14: Motor Controllers
Two types of motor controllers:
  Simple motor controllers: controls brushed DC motors, no built-in microcontrollers, communicates with RoboRIO via PWM (Pulse Width Modulation).
  Smart motor controllers: controls brushed or brushless DC motors, built-in microcontrollers, communicates with RoboRIO via CAN bus.

## Slide 15: Simple Motor Controllers
Simple motor controllers are dumb controllers without built-in processors.
Communicates with the RoboRIO via PWM (Pulse Width Modulation: 1 ms full speed reverse, 1.5 ms stop, 2 ms full speed forward).
Our framework supports: FrcPWMSparkMax, FrcPWMTalonFX, FrcPWMTalonSRX, FrcPWMVictorSPX and generic. Constructors: FrcPWMVictorSPX(String instanceName, int pwmChannel, Encoder encoder, FrcDigitalInput revLimitSw, FrcDigitalInput fwdLimitSw)
Useful Methods: void setInverted(boolean inverted) void stopMotor() void set(double delay, double value, double duration) void set(double value)

## Slide 16: Exercise: Simple Motor Controllers
In Robot.java, create a PWM motor controller.
  Create a class variable (pwmMotor) to hold the created PWM motor controller object (e.g. FrcPWMTalonSRX).
  In robotInit method, create the motor controller object specifying a name and the PWM channel it’s plugged into.
In FrcTeleOp.java, add code in the periodic method to control a motor connected to the motor controller by a game controller and print a message showing the motor power on the dashboard.
  Read the Xbox left stick for the Y-axis (robot.driverController.getLeftYWithDeadband).
  Set the motor power with the joystick value (robot.pwmMotor.set).
  Display the motor power value to the dashboard (robot.dashboard.displayPrintf).

## Slide 17: Smart Motor Controllers
Smart motor controllers have built-in processors.
Communicates with the RoboRIO via CAN bus.
RoboRIO can issue CAN command to control the direction as well as the speed of the motor.
Supports position sensors (e.g. encoder or analog potentiometer) to perform close-loop control (e.g. position control or speed control).
Supports hardware limit switches to limit motor movement within a range of physical positions.
Our framework supports: FrcCANFalcon, FrcCANTalon, FrcCANSparkMax.
Constructors: FrcCANFalcon(String instanceName, int canID) FrcCANTalon(String instanceName, int canID) FrcCANSparkMax(String instanceName, int canID, boolean brushless)
Useful Methods: void setInverted(boolean inverted) void stopMotor() void set(double value) void set(double delay, double value, double duration)

## Slide 18: Exercise: Smart Motor Controllers
In Robot.java, create a Talon SRX motor controller.
  Create a class variable (canMotor) to hold the created smart motor controller object (e.g. FrcCANTalon).
  In robotInit method, create the motor controller object specifying a name and its assigned CAN ID.
In FrcTeleOp.java, add code to control a motor connected to the motor controller by a game controller and print a message showing the motor power on the dashboard.
  Read the Xbox left stick for the Y-axis (robot.driverController.getLeftYWithDeadband).
  Set the motor power with the joystick value (robot.canMotor.set).
  Display the motor power value to the dashboard (robot.dashboard.displayPrintf).

## Slide 19: TrcMotor
All motor controller classes extend TrcMotor including PWM motor controllers and smart motor controllers. Different motor controllers have different capabilities. TrcMotor simulates features that the motor controller does not have native support, using software wherever possible. Examples:
  Simulates close-loop control for PWM motor controllers with software PID and external position sensor.
  Simulates limit switch protection for PWM motor controllers with external limit switches.
TrcMotor features with software simulation:
  Motor direction.
  Motor followers.
  Position sensor direction.
  Motor odometry (position, velocity, current).
  Limit switches.
  Close-loop control (position control, velocity control).
  Motor stall detection/protection.
  Motor zero position calibration.

## Slide 20: Servo Motors
Three types of servo motors:
  Position servos: have limited range of motion usually 90-degree or 180-degree, communicate via PWM signal between 1 ms to 2 ms. Pulse width sets the position of the servo. For example, for 180-degree servo, 1 ms sets it to 0-degree, 1.5 ms sets it to 90-degree and 2 ms sets it to 180-degree.
  Continuous servos: similar to DC motors on PWM motor controllers but with smaller form factor and weaker strength, communicate via PWM signal between 1 ms to 2 ms. Pulse width sets the direction and speed the servo will spin. 1 ms sets it to spin full speed in reverse, 1.5 ms sets it to stop and 2 ms sets it to spin full speed forward.
  Digital servos: programmable servo that can be programmed as position servo or continuous servo, can change servo parameters such as the position range, deadband in continuous mode etc.
Constructors: FrcServo(String instanceName, int pwmChannel)
Useful Methods: void setInverted(boolean inverted) void setPosition(double position) //for position servo void setPower(double power) //for continuous servo

## Slide 21: Exercise: Position Servo
In Robot.java, create a servo motor.
  Create a class variable (servo) to hold the created servo motor object (e.g. FrcServo).
  In robotInit method, create the servo motor object specifying a name and the PWM channel it’s plugged into.
In FrcTeleOp.java, add code in the periodic method to control a servo by using the left trigger of the Xbox controller. (i.e. releasing it to go to 0-degree position and pressing it fully to go to 180-degree) and print a message on the dashboard to show the servo position.
  Read the Xbox left trigger (robot.driverController.getLeftTriggerWithDeadband).
  Set the servo position with the trigger value (robot.servo.setPosition).
  Display the servo position to the dashboard (robot.dashboard.displayPrintf).

## Slide 22: Relay
Relay is a switch. It has three states:
  OFF: Output is disconnected from the input power.
  FWD: Positive output is connected to positive power, negative output is connected to negative power.
  REV: Positive output is connected to negative power, negative output is connected to positive power.
It can be used to control a motor. Setting the relay to OFF stops the motor, FWD spins full speed in forward direction, REV spins full speed in reverse direction. Unlike motor controllers, relay does not regulate the motor speed. It’s either ON or OFF.
It is commonly used as an ON/OFF switch to LED lights. For example, the ring light used in vision.
Constructors: Relay(int channel, Direction direction) channel – specifies relay channel direction – specifies kBoth, kForward or kReverse
Methods: void set(Value value) //values are: kOff, kOn, kForward, kReverse Value get()

## Slide 23: Exercise: Control Ring Light with a Button
Control a camera ring light with a button on the game controller.
  In Robot.java, add code to robotInit to create a relay in kForward direction mode (Relay).
  In FrcTeleOp.java, add code to driverControllerButtonEvent to toggle the ring light ON/OFF with pressing the A button. Print a message on the dashboard to show the ring light state.

## Slide 24: Pneumatics
Pneumatics are devices actuated by compressed air. They have a piston that extends and retracts when compressed air is pumped into one side or the other side of the cylinder.
Two types of pneumatics cylinders: one valve or two valves. 2-valve allows air to pump into one side or the other side to extend or retract. 1-valve allows air to pump into the cylinder to extend. Retraction is by spring.
Components of a pneumatic system: compressor, air tanks, pressure regulators, pressure sensor switch, pressure relief valve and cylinder valves. Compressor turns on to fill air tanks up to the maximum pressure of 110-120 psi which trips the pressure sensor switch to stop the compressor. Pneumatic Control Hub (PCH) is a CAN bus device that receives commands from RoboRIO to turn valves ON or OFF. PCH supports 16 channels. 2-valve pneumatic cylinder requires 2 channels (extend and retract).
Constructors: FrcPneumatic(String instanceName, int pchCANId, PneumaticsModuleType moduleType, int channel) //for 1-valve FrcPneumatic(String instanceName, int pchCANId, PneumaticsModuleType moduleType, int channel1, int channel2) //for 2-valve
Useful Methods: void extend() void retract() boolean isExtended()

## Slide 25: Exercise: Pneumatics
In Robot.java, create a 2-valve pneumatic cylinder.
  Create a class variable (piston) to hold the created pneumatic cylinder (e.g. FrcPneumatic).
  In robotInit method, create the servo motor object specifying a name and the PWM channel it’s plugged into.
In FrcTeleOp.java, add code to the buttonEvent handler of the game controller (driverControllerButtonEvent) to control the the pneumatic valves connected to the PCH channels by a game controller button (press to extend, release to retract) and print a message showing the pneumatic valve state on the dashboard.
  On the button X pressed event, extends the pneumatic piston (robot.piston.extend).
  On the button X released event, retracts the pneumatic piston (robot.piston.retract).
  Display the piston state on the dashboard (robot.dashboard.displayPrintf, robot.piston.isExtended).

## Slide 26: Sensors
Two types of sensors: Digital sensors and Analog sensors.
Digital Sensors have two states: active, inactive (e.g. limit switches, beam break sensors).
Analog sensors provide analog values (e.g. ultrasonic, LIDAR, pressure sensor, color sensor, gyro, accelerometer etc).
FrcDigitalInput constructors: FrcDigitalInput(String instanceName, int dioChannel)
FrcDigitalInput useful methods: void setInverted(boolean inverted) boolean isActive()
FrcAnalogInput constructors: FrcAnalogInput(String instanceName, int analogChannel)
FrcAnalogInput useful methods: void calibrate() SensorData<Double> getRawData(int index, DataType dataType)

## Slide 27: Exercise: Digital Sensor
In Robot.java, create a limit switch.
  Create a class variable (limitSwitch) to hold the created digital input object (e.g. FrcDigitalInput).
  In robotInit method, create the limit switch object specifying a name and the DIO channel it’s plugged into.
In FrcTeleOp.java, add code to the periodic method to print a message showing the state of the limit switch on the dashboard.
  On the button X pressed event, extends the pneumatic piston (robot.piston.extend).
  On the button X released event, retracts the pneumatic piston (robot.piston.retract).
  Display the piston state on the dashboard (robot.dashboard.displayPrintf, robot.piston.isExtended).

## Slide 28: Exercise: Analog Sensor
In Robot.java, create a REV color sensor.
  Create a class variable (colorSensor) to hold the created analog sensor object (e.g. ColorSensorV3).
  In robotInit method, create the color sensor specifying the I2C port it’s plugged into.
In FrcTeleOp.java, add code to the periodic method to print a message showing the color sensor values on the dashboard.
  Display the color sensor values on the dashboard (robot.dashboard.displayPrintf, robot.colorSensor.getProximity, robot.colorSensor.getRed, robot.colorSensor.getGreen, robot.colorSensor.getBlue).

## Slide 29: Digital Sensor Trigger
Digital trigger provides an asynchronous mechanism to detect digital sensor state changes. It monitors the digital sensor and will do a callback when state change occurs. By default, the digital trigger is created disabled so you need to explicitly enable the monitoring and disable it when it’s no longer needed.
TrcDigitalInputTrigger constructors: TrcDigitalInputTrigger(String instanceName, TrcDigitalInput sensor, TrcEvent.Callback triggerCallback)
TrcDigitalInputTrigger useful methods: void setEnabled(boolean enabled) boolean isEnabled() boolean getSensorState()
Digital Trigger callback method: void digitalTriggerCallback(Object context)
Digital Trigger callback context is an AtomicBoolean. It gives you the digital sensor state that caused the trigger: ((AtomicBoolean) context).get()

## Slide 30: Exercise: Digital Sensor Trigger
In Robot.java, create a limit switch and a digital trigger.
  Create a class variable (limitSwitch) to hold the created digital input object (FrcDigitalInput).
  Create a class variable (limitSwitchTrigger) to hold the created digital trigger (TrcDigitalInputTrigger).
  In robotInit method, create the limit switch object specifying a name and the DIO channel it’s plugged into.
  In robotInit method, create the digital trigger specifying a name, the limitSwitch object as the sensor and the callback method to call when the trigger occurs.
  Create the trigger callback method: private void limitSwitchTriggerCallback(Object context)
  In the callback method, print a message showing the state of the limit switch on the dashboard. Hint: ((AtomicBoolean) context).get() returns the state of the limit switch

## Slide 31: Analog Sensor Trigger
Analog trigger provides an asynchronous mechanism to detect sensor value crosses preset thresholds. It monitors the analog sensor and will do a callback when a threshold has been crossed.
TrcAnalogSensorTrigger constructors: TrcAnalogSensorTrigger(String instanceName, TrcSensor<D> sensor, int index, D dataType, double[] dataPoints, boolean dataIsTrigger, TrcEvent.Callback triggerCallback)
TrcAnalogSensorTrigger useful methods: void setEnabled(boolean enabled) boolean isEnabled() double getSensorValue()
Analog Trigger callback method: void analogTriggerCallback(Object context)
Analog Trigger callback context is a TrcAnalogSensorTrigger.CallbackContext object. It gives you the state of the analog trigger at the time of the trigger: ((TrcAnalogSensorTrigger.CallbackContext) context).sensorValue ((TrcAnalogSensorTrigger.CallbackContext) context).prevZone ((TrcAnalogSensorTrigger.CallbackContext) context).currZone

## Slide 32: Exercise: Analog Sensor Trigger
In Robot.java, create a REV color sensor, an analog sensor that wraps around the REV color sensor to make it compatible with our framework and an analog trigger.
  Create a class variable (revColorSensor) to hold the created REV color sensor (ColorSensorV3).
  Create a class variable (colorSensor) to hold the created analog sensor (TrcAnalogSensor).
  Create a class variable (colorSensorTrigger) to hold the created analog trigger (TrcAnalogSensorTrigger).
  In robotInit method, create the REV color sensor object specifying the I2C port it’s plugged into.
  Create the analog sensor object specifying a name and the method to call to get the color sensor value (getColorSensorValue).
  Create an array of doubles containing the trigger threshold values.
  Create the analog trigger specifying a name, the created analog sensor, zero as the index, TrcAnalogInput.DataType.INPUT_DATA as the data type, the threshold array, false as dataIsTrigger and the method to call when the trigger occurs.
  Create the getColorSensorValue method that returns the proximity value of the REV color sensor (revColorSensor.getProximity).
  Create the trigger callback method: private void colorSensorTriggerCallback(Object context)
  In the callback method, print a message showing the state of the color sensor on the dashboard. Hint: TrcAnalogSensorTrigger.CallbackContext colorSensorContext = (TrcAnalogSensorTrigger.CallbackContext) context; colorSensorContext.sensorValue returns the color sensor value colorSensorContext.prevZone returns the previous threshold zone colorSensorContext.prevZone returns the current threshold zone

## Slide 33: Indicators
Indicators are used to give feedback to the human operators. Our framework supports the following categories:
  Single LED: (FrcDigitalOutput)
  LED strip: single color, RGB (FrcRevBlinkin)
  Addressable LED strip: each pixel on the strip can be programmed to a different color (FrcAddressable LED, FrcRevBlinkin)
  LED Panel: (FrcI2cLEDPanel)
  Speech: Emic2 Text to Speech controller (FrcEmic2TextToSpeech)
  TrcTone, TrcSong: supports generating sound and play songs (more for FTC and not really for FRC because FRC robot controller does not support sound).

## Slide 34: Priority Indicators
Using LEDs as an indicator device allows subsystems to display their status.
Problem: Multiple subsystems trying to send their status to the LED causing contention.
Solution: Priority Indicator (TrcPriorityIndicator).
  Each subsystem creates different indicator patterns. TrcPriorityIndicator keeps a table with these patterns stored in priority order (lowest priority first).
  Subsystem turns on an indicator pattern. TrcPriorityIndicator has a task going through the table periodically to find the highest priority pattern that is ON and display it. When the highest priority pattern is turned off, the next highest priority pattern will be displayed.
Useful methods: void setPatternState(T pattern, boolean enabled, double expiredTime) setPatternState not only allows you to turn a pattern ON or OFF, you can also specify an expiredTime so it will turn itself off after the specified period. This is good for indicating an edge event or creating a blinking pattern.

## Slide 35: Exercise: Priority Indicators
In subsystems\LEDIndicators.java, create a new TrcAddressableLED.Patterns named buttonXPattern and set it to solid green color.
Create another pattern named buttonYPattern and set it to solid yellow color.
Add the buttonXPattern to be the highest priority pattern in the priorities array.
Add the buttonYPattern to be the next highest priority pattern in the priorities array.
Add two methods that enables or disables the buttonXPattern and buttonYPattern states according to the pressed parameter (Hint: led.setPatternState). void setXButtonState(boolean pressed) void setYButtonState(boolean pressed)
In FrcTeleOp.java, add code to the driversControllerButtonEvent method to call setXButtonState enabling the LED pattern when button X is pressed, disabling it when button X is released.
Similarly, add code to call setYButtonState enabling the LED pattern when button Y is pressed, disabling it when button Y is released.