## Slide 1: Advanced Robotics Programming Class Lesson 2: Introduction to TRC Library
Titan Robotics Club FRC492
Michael Tsang (Programming Mentor)

## Slide 2: Agenda
TRC Library Organization
TRC Library: Input
TRC Library: Output
TRC Library: System

## Slide 3: TRC Library Organization
TRC Library is the core of our robot code. Its benefits include:
  Literally avoid re-inventing the wheel every season and allow us to focus on coding competition strategies.
  Library code has been tested extensively every season and therefore very stable.
  Provide a mechanism to pass on knowledge from one generation to the next allowing us to create increasingly complex robot strategies.
TRC Library architecture allows sharing between FTC and FRC: The layering approach.
  TrcLib: Common code identical to both FTC and FRC (majority of the framework).
  HalLib: Hardware Abstraction Layer, identical interfaces but different implementation for FTC and FRC.
  FtcLib, FrcLib: FTC and FRC specific libraries.
TRC Library is organized into three categories and sub-categories within them:
  Input: Driver Station, Sensors
  Output: Indicators, Actuators
  System: Drive Base, Motion, Filters, Vision, Protocols, Multitasking, Utilities, Diagnostics
  JavaDoc is available here.

## Slide 4: Input: Driver Station
Example classes:
  FrcJoystick: supports a typical game joystick.
  FrcXboxController: supports an Xbox game controller.
  FrcButtonHandler: contains the button handler interface.
  FrcChoiceMenu: supports interacting with choice menus on SmartDashboard.
  …

## Slide 5: Input: Sensors
Example classes:
  FrcAHRSGyro: supports the KauaiLabs NavX Robotics Navigation Sensor.
  FrcAnalogSensor, FrcAnalogInput: supports generic Analog sensors such as potentiometers.
  TrcTrigger: monitors trigger points of analog sensors.
  FrcDigitalInput: supports generic digital sensor such as limit switches.
  FrcCANTimeOfFlight: supports CAN based Time-of-Flight distance sensor.
  FrcGryo: supports generic Analog Gyros.
  FrcPdp: monitors the FRC Power Distribution Panel.
  FrcRobotBattery: monitors the robot battery voltage.
  FrcPixyCam1, FrcPixyCam2: supports Pixy Camera generation 1 and 2 respectively.
  …

## Slide 6: Output: Indicators
Example classes:
  FrcDigitalOutput: supports generic digital output, can be used to control lights.
  FrcAddressableLED, FrcDigitalRGB, FrcI2cLEDPanel, FrcRGBLights, TrcPriorityIndicator: supports various LED lights.
  FrcRevBlinkin: supports REV Blinkin LED light controller.
  FrcEmic2TextToSpeech: supports Emic2 Text to Speech controller.
  TrcTone, TrcSong: supports generating sound and play songs.
  …

## Slide 7: Output: Actuators
Example classes:
  FrcDigitalOutput: support generic digital output, can be used to control solenoids.
  FrcCANTalon: supports CAN Talon motor controllers.
  FrcCANSparkMax: supports CAN SparkMax motor controllers.
  FrcCANFalcon: supports CAN Falcon motor controllers.
  FrcPneumatics: supports Pneumatic actuators.
  TrcServo, TrcEnhancedServo: supports generic servo motors.
  TrcSwerveModule: supports Swerve Drive modules.
  TrcPidDrive: supports PID controlled drive.
  TrcPidActuator: supports PID controlled actuators (e.g. elevator)
  …

## Slide 8: System: Drive Base
Example classes:
  TrcSimpleDriveBase: supports simple tank type Drive Base up to 6 motors.
  TrcMecanumDriveBase: supports 4-wheel Mecanum Drive Base.
  TrcSwerveDriveBase: supports 4-wheel Swerve Drive Base.
  …

## Slide 9: System: Motion Drive
Example classes:
  FrcTankMotionProfileFollower: supports Motion Profiling using Tank Drive Base.
  TrcHolonomicPurePursuitDrive: supports Pure Pursuit Drive using Holonomic Drive Base.
  …

## Slide 10: System: Data Filters
Example classes:
  TrcHighPassFilter, TrcMedianFilter, TrcMovingAverageFilter, TrcIIRFilter, TrcKalmanFilter: filtering sensor noise.
  TrcSpuriousFilter: filtering out spurious sensor data.
  TrcCardinalConverter: convert between cardinal and cartesian systems.
  TrcDataIntegrator: integrate data (e.g. integrate gryo angular velocity into heading).
  TrcWarpSpace: convert linear space into warp space.
  …

## Slide 11: System: Vision Processing
Example classes:
  FrcOpenCVDetector: supports OpenCV object detection.
  FrcRaspiVisionProcessor: supports Raspberry Pi Vision Processing.
  FrcLimeLightVisionProcessor: supports Lime Light Vision Processing.
  FrcRemoteVisionProcessor: supports generic remote Vision Processing.
  FrcFaceDetector: supports human face detection.
  …

## Slide 12: System: Communication Protocols
Example classes:
  TrcSerialPortDevice: supports Serial Port devices.
  TrcI2cDevice: support I2C devices.
  TrcSpiDevice: support SPI devices.
  …

## Slide 13: System: Multitasking
Example classes:
  TrcEvent: supports event notification by polling.
  TrcNotifier: supports event notification by callback.
  TrcStateMachine: supports state machines.
  TrcRequestQueue: supports asynchronous request queue (First-In-First-Out)
  TrcExclusiveSubsystem, TrcOwnershipManager: supports exclusive subsystems.
  TrcPeriodicThread, TrcTaskMgr: support multi-threading.
  …

## Slide 14: System: Utilities
Example classes:
  TrcBooleanState: supports Boolean state object.
  TrcElapsedTimer, TrcIntervalTimer, TrcStopwatch: various timing supports.
  TrcTimer, TrcTimerMgr: support event timers.
  TrcHashMap: supports generic Hash Map.
  TrcUtil: Miscellaneous utility methods (e.g. Math tools, system time tools etc).
  …

## Slide 15: System: Diagnostics
Example classes:
  TrcDbgTrace: supports debug tracing.
  TrcTraceLogger: supports logging.
  TrcDiagnostics: supports diagnostic test collections.
  TrcTestAnalogSensorValueChange: supports diagnostics tests to monitor if an analog sensor value has changed.
  TrcTestDigitalSensorStateChange: supports diagnostics tests to monitor if a digital sensor state has changed.
  …