## Slide 1: Advanced Robotics Programming Class Lesson 6: Multi-tasking and Threads
Titan Robotics Club FTC3543
Michael Tsang (Programming Mentor)

## Slide 2: Agenda
In this lesson, you will learn everything about Multi-Tasking and Threads:
  Multi-tasking Explained
  Task
  Main Robot Thread
  Other Threads
  Task Manager
  Cautions On Multi-Tasking
  Asynchronous Support
  State Machine
  Event
  Subsystem Exclusive Ownership

## Slide 3: Multi-tasking Explained
Because of the short 30-second autonomous period, we must try performing operations that don’t depend on each other in parallel.
Multi-tasking real life example: You have a birthday party coming up and your mom wants you to finish your home work, do the laundry as well as baking your own pizza for the party. So you have three tasks (finish homework, do laundry, bake pizza).
Task 1: do laundry (total time – 2 hours)
  Put clothes into washing machine.
  Put in laundry detergent.
  Start washing machine.
  Wait for the washing machine to beep.
  Move the clothes into the dryer.
  Put in fabric softener sheet.
  Start dryer.
  Wait for the dryer to beep.
  Take clothes out, fold them and put away.
Task 2: bake pizza (total time – 0.5 hour)
  Wait until half hour before party start.
  Set oven to preheat to 450˚F.
  Wait for the oven to beep.
  Put the frozen pizza into the oven.
  Set timer for 20 minutes.
  Wait for the oven to beep.
  Take pizza out and cut into 8 pieces.
  Put on plates and serve guests.

## Slide 4: Multi-tasking Explained (continue)
To do all these tasks, one could do task 1 to its completion before starting task 2. After task 2 is completed then starts task 3. But it will be a waste of time and most of the time spent is waiting.
Multi-task is a better way. Note that there are operations in the task just simply waiting. Instead of staring at the washing machine or the oven waiting for it to beep, switch to the other tasks to make progress.
Combined tasks:
  Do task 1 operations 1-3.
  Operation 4 is to wait for the washing machine to beep, switch to task 2 and check if you are about half an hour before the birthday party starts. If not, switch to task 3 to do your homework until you hear the washing machine beeps or it is about half an hour before the party starts.
  If the washing machine beeps, switch back to task 1, do operations 5-7. Then switch to task 2 and check if you are about half hour before the birthday party starts. If not, switch back to task 3 and continue doing your homework.
  When it’s about half hour before the party starts, switch back to task 2 and do operation 2.
  Switch back to task 3 to continue doing your homework.
  When oven beeps, switch back to task 2 and do operations 4-5.
  Switch back to task 3 to continue doing your homework.
  When the dryer beeps, switch back to task 1 and do operation 9.
  When done, switch back to task 3 to continue doing your homework. Homework is now done.
  Switch back to task 2 and wait for oven to beep, then finish operations 7-8.

## Slide 5: Task
Task is multi-tasking unit in our framework. It contains code to be run in a multi-tasking thread. You can register a task to be execute at a certain time by a certain thread.
In Titan Robotics Framework, there are many task types you can register:
  START_TASK – runs in the main robot thread before a robot mode starts.
  STOP_TASK – runs in the main robot thread before a robot mode stops.
  PRE_PERIODIC_TASK – runs in the main robot thread before periodic method is called.
  POST_PERIODIC_TASK – runs in the main robot thread after periodic method is called.
  INPUT_TASK – runs in the IO thread before all OUTPUT_TASK.
  OUTPUT_TASK – runs in the IO thread after all INPUT_TASK.
  STANDALONE_TASK – runs in a standalone thread.

## Slide 6: Main Robot Thread
When the robot is powered up, the following sequence is executed in the main robot thread.
  Execute Robot.robotInit method to create/initialize robot hardware, set initial robot mode to DisabledMode.
  Execute Robot.robotStartMode method to initialize robot not specific to the robot mode.
  Execute TrcRobot.RobotMode.startMode method to initialize robot specific to the robot mode.
  Execute all registered START_TASK.
  If periodic ready, execute all registered PRE_PERIODIC_TASK.
  If periodic ready, execute periodic method.
  If periodic ready, execute all registered POST_PERIODIC_TASK.
  If robot is staying in the same mode, go back to step 5, otherwise go to next step.
  Execute all registered STOP_TASK.
  Execute TrcRobot.Robot.RobotMode.stopMode method to do cleanup specific to the previous robot mode.
  Execute Robot.robotStopMode method to do cleanup not specific to the robot mode.
  End of OpMode.

## Slide 7: Other Threads
IO Thread: All registered INPUT_TASKs and OUTPUT_TASKs run in the IO Thread. Generally deals with reading sensors and input states (INPUT_TASK), also deals with any kind of actuators and status indicators (OUTPUT_TASK).
Standalone Thread: Every registered STANDALONE_TASK has its own thread. Generally used for very high performance tasks that require high frequency execution and low latency or tasks that take a long time to execute and will impact other tasks on the same thread if they don’t have their own thread.

## Slide 8: Task Manager
TrcTaskMgr manages tasks. It provides methods to create/register/unregister tasks of different task types.
TrcTaskMgr is a singleton that exists on first use: TrcTaskMgr.getInstance()
Once you obtain the TaskMgr instance, it provides the following method to create a task object:
  createTaskObj – instance name of the task and reference to the method that contains the code for the task.
The task object provides the following methods:
  registerTask – task type the task will be registered for. A task can register for multiple task types.
  unregisterTask – task type the task will be unregistered or to unregister all task types.
When a task is registered for a task type, its task method will be called at the appropriate time on the appropriate thread depending on the task type.

## Slide 9: Cautions on Multi-tasking
Since multi-tasking involves multiple threads (main robot thread, IO thread and some number of standalone threads), care must be taken to understand problems introduced in this kind of environment which are derived from two main issues.
  Resource contention – shared access to data.
  Synchronization – coordination between different threads.
Resource contention: shared data between multiple threads can be easily corrupted seemingly randomly. Solution is controlled atomic access to shared data (acquire lock before shared data is access and release lock afterwards).
Synchronization: multiple threads can run with different speeds. When one thread’s execution depends on results from another thread, one must make sure these threads are synchronized so one thread will get the proper result from another thread at appropriate time. Solution is synchronization notifications.
Solutions to these problems sometimes create more problems: e.g. deadlock or performance issues. That’s why multi-thread programming is really hard. Should avoid it if possible. If unavoidable, try minimizing the problems: limit data sharing and the need for synchronization.
Fortunately, Titan Robotics Framework provides some mechanisms that will help in some aspects of multi-tasking. For example, TrcEvent provides synchronization notifications between threads. It also provides cooperative multi-tasking that runs tasks on the main robot thread. This eliminates the issue of shared resource contention.

## Slide 10: Asynchronous Support
Everything in our library supports asynchronous. It means if an operation takes time to finish, calling it will start the operation but it will return immediately and hand the actual work to another task monitoring the progress. It will not keep you waiting for it to get done. This allows your code to perform something else while the other operation is in progress. However, if another operation depends on the previous operation to be done before it can start, we need a way to synchronize the two operations.
To support asynchronous operations, we need three ingredients:
  Ability to notify somebody when the operation has completed. This is where event comes in to help.
  Ability to suspend a task while waiting for operation(s) to finish and keep track of the next state so the code can make progress on other tasks and be able to resume the task to the next state when the current operation is completed. This is where state machine comes in to help.
  Ability to request exclusive ownership of subsystems while an operation is using them so that other tasks cannot interfere with their operations.
It is sometimes helpful to group a number of operations into an AutoTask that can be used in Autonomous as well as an auto-assist operation used in TeleOp.

## Slide 11: State Machine
TrcStateMachine implements a state machine that keeps track of the state of a task. A state represents the step the task is executing. When the task is waiting for a step to finish, the task is put into waiting mode so the robot can switch to other tasks.
Every time the robot switches tasks, it checks which task has finished waiting (i.e. ready to run) and will resume that task to make progress. By doing this, every task has a chance to make progress when other tasks are waiting.
TrcStateMachine<T> Constructor: instance name.
Methods:
  start – starts the state machine with the given state (enable state machine and set initial state to the given state).
  stop – terminates the state machine (disable state machine).
  getState – returns the current state the task is in (return null if state machine is not started).
  setState – set the state machine to the given state.
  isEnabled – check if the state machine is enabled (i.e. started).
  isReady – check if the state machine is waiting (i.e. not ready).
  isTimedout – check if the condition the state machine is waiting has timed out.
  addEvent – add an event to the list of things the state machine is waiting for.
  clearAllEvents – clear the event list.
  waitForEvents – put the state machine in waiting mode waiting for the events on the list; have option to wait for any one event or all events on the list.
  waitForSingleEvent – same as waitForEvents except there is just one event, not a list of events.
  checkReadyAndGetState – if state machine is waiting, it will check the event lists for any signaling event(s). If so, the state machine will move to the next state; then it returns the current state of the state machine.

## Slide 12: Event
Event is the synchronization mechanism in multi-tasking. It is a flag indicating something has finished or canceled. Most components in the TRC library starts an operation and returns immediately (i.e. Asynchronous). The operation will be performed on a separate task. When it is done or canceled, it will signal an event. State machine uses events to determine if a task should be resumed to continue to the next state.
Event has three states: cleared, signaled and canceled.
TrcEvent Constructor: TrcEvent(String instanceName)
Methods:
  void clear() – set the event to cleared state.
  void signal() – set the event to signaled state.
  void cancel() – set the event to canceled state.
  boolean isSignaled() – check if the event is in signaled state.
  boolean isCanceled() – check if the event is in canceled state.
  void setCallback(Callback callback, Object callbackContext) – set the method to call back when the event is signaled or canceled.

## Slide 13: Subsystem Exclusive Ownership
In a multi-tasking environment, multiple tasks may try to take control of various subsystems. For example: human control in TeleOp could interfere with auto-assist operations. Solution: to operate a subsystem in an auto-assist task, one must acquire exclusive ownership to the subsystem before proceeding.
TrcOwnershipMgr: A singleton that manages subsystem ownership. It exists when the robot program is running. It provides the following methods:
  acquireOwnership: specifies the owner’s ID and the subsystem to acquire ownership.
  releaseOwnership: specifies the owner’s ID and the subsystem to release ownership.
  hasOwnership: checks if the specified owner has the ownership of the susbsystem.
  validateOwnership: checks if the specified owner has the ownership of the subsystem, throws an exception if not.
  getOwner: get the owner ID of the subsystem.

## Slide 14: How Does Subsytem Ownership Work?
To make a subsystem support ownership, it must implement the TrcExclusiveSubsystem interface which means it must provide the following methods:
  acquireExclusiveAccess
  releaseExclusiveAccess
  hasOwnership
  validateOwnership
Don’t really need to write any code for the above methods because TrcOwnershipMgr provides default implementations for them and that’s all you need.
For actions that may be called by different callers that could cause conflict, the actions must be called specifying the caller’s ID so that it will check for ownership.
For Auto-Assist modules, they must acquire ownership before calling Exclusive Subsystems and release ownership when done.