## Slide 1: Advanced Robotics Programming Class Lesson 8: Complex Subsystems
Titan Robotics Club FRC492
Michael Tsang (Programming Mentor)

## Slide 2: Agenda
In this lesson, you will learn:
  Complex Subsystems
    Conveyor
    Intake
    Shooter
  Subsystem ownership

## Slide 3: Infinite Recharge Conveyor Subsystem
Conveyor subsystem contains conveyor motor and two proximity sensors. Frc2020InfiniteRecharge/Conveyor.java at master · trc492/Frc2020InfiniteRecharge (github.com)
TeleOp Controls:
  Trigger: press to shoot.
  Button 2: run the conveyor forward when pressed, stop when released.
  Yellow1 Button: run the conveyor backward when pressed, stop when released.
  Blue2 Switch: turn on/off conveyor manual override.
  Red1 Button: when pressed and in manual override mode, advance the conveyor one ball space.
InTake task: run the conveyor if there is a ball at the entrance and no ball at the exit.
Advance task: monitor conveyor move distance for one ball space and notify caller.
Monitor exit proximity sensor events: to decrease ball count, notify somebody after a ball is shot and stop the shooter.
Provide the following actions:
  setPower – manually running conveyor at given power.
  intake – run the InTake task to in take more balls.
  shoot – deliver a ball to the shooter and shoot.
  advance – advance the conveyor by the given distance (default distance: one ball space).
  setManualOverrideEnabled – enable/disable manual override mode.

## Slide 4: Infinite Recharge InTake Subsystem
InTake subsystem contains intake motor and intake extender pneumatics. Frc2020InfiniteRecharge/Intake.java at master · trc492/Frc2020InfiniteRecharge (github.com)
TeleOp Controls:
  Button 4: extend intake pneumatics when pressed.
  Button 5: retract intake pneumatics when pressed.
  Button 3: start intake task state machine when pressed to perform a sequence of actions.
InTake task state machine:
  BACKUP: tell the conveyor to back up balls until either a ball triggers the entrance proximity sensor or it backs up enough to prove there is no ball in the conveyor.
  FORWARD: tell the conveyor to advance the distance of the ball spacing.
  INTAKE: spin intake motor to pick up balls until a ball triggers the exit proximity sensor.
  MONITOR: if entrance proximity sensor detected a ball, go to the ADVANCE state.
  ADVANCE: tell the conveyor to advance the ball until it past the entrance proximity sensor and stop.
  SECURE: readjust the ball to have the specified spacing between the new ball and the balls in the conveyor.

## Slide 5: Infinite Recharge Shooter Subsystem
Shooter subsystem contains shooter motor and pitch motor. Frc2020InfiniteRecharge/Shooter.java at master · trc492/Frc2020InfiniteRecharge (github.com)
TeleOp Controls:
  Operator Stick Y: Control shooter pitch when manual override is ON.
  Operator Stick Z: Control shooter motor when manual override is ON.
  Xbox Controller Right Bumper: Press to use auto shooter to track target.
  Operator Button 6: Press to aim and shoot high goal, release to stop.
  Operator Button 7: Press to aim and shoot low goal, release to stop.
  Operator Button 8: Stow shooter.
  Operator Button 9: Reset all shooter related subsystems.
  White1 Button: Reset some shooter related subsystems.
  Green2 Switch: Turn shooter manual override ON/OFF.
Pitch Control Task: monitor if pitch has reached target and notify caller.
Provide the following actions:
  setPitchPower – manually running pitch motor at given power.
  setPitch – set pitch angle.
  setFlywheelVelocity – set shooter motor speed.
  stopFlywheel – shut down shooter motor.
  stowShooter – set shooter pitch down to bottom.
  setManualOverrideEnabled – enable/disable manual override mode.

## Slide 6: Subsystem Ownership
In a multi-tasking environment, multiple tasks may try to take control of different subsystems. For example: human control in TeleOp could interfere with auto-assist operations. Solution: to operate a subsystem, one must acquire ownership to the subsystem before proceeding.
TrcOwnershipMgr: A singleton that manages subsystem ownership. It exists when the robot program is running. It provides the following methods:
  acquireOwnership: specifies the owner’s ID and the subsystem to acquire ownership.
  releaseOwnership: specifies the owner’s ID and the subsystem to release ownership.
  hasOwnership: checks if the specified owner has the ownership of the susbsystem.
  validateOwnership: checks if the specified owner has the ownership of the subsystem, throws an exception if not.
  getOwner: get the owner ID of the subsystem.

## Slide 7: How Does Subsytem Ownership Work?
To make a subsystem support ownership, it must implement the TrcExclusiveSubsystem interface which means it must provide the following methods:
  acquireExclusiveAccess
  releaseExclusiveAccess
  hasOwnership
  validateOwnership
Don’t really need to write any code for the above methods because TrcOwnershipMgr provides default code for them.
For actions that may be called by different callers that could cause conflict, the actions must be called specifying the caller’s ID so that it will check for ownership.
For Auto-Assist modules, they must acquire ownership before calling Exclusive Subsystems and release ownership when done.