## Slide 1: Advanced Robotics Programming Class Lesson 1: Introduction to Titan Robotics Framework
Titan Robotics Club FTC3543
Michael Tsang (Programming Mentor)

## Slide 2: Advanced Robotics Programming Class
Titan is using Java as the programming language for both FTC and FRC.
We developed an extensive Java Robotics Framework shared between FTC and FRC.
This class focuses on learning how to use this framework.
What this class doesn’t cover: We don’t teach Java language here. We assume you are proficient in writing Java code. If you need to learn Java, you need the Beginner Class or there are many on-line resources learning Java.
Notes: Make sure students are at the correct level (poll for Java knowledge)

## Slide 3: Agenda
In this lesson, we will learn about the Titan Robotics Framework:
  Software Installation
  What is TRC Framework?
  TRC Framework Organization
  FTC Template Project
  Robot Code Organization
  FTC Robot Modes
  FTC OpModes: FtcAuto, FtcTeleOp, FtcTest
  OpMode Execution Flowchart
  Robot.java
  Robot Organization
  RobotParams.java

## Slide 4: Software Installation
GitHub: That's where all our code repositories are stored. If you don't already have a GitHub account, register for one here. Our code repositories can be found here.
Follow the software installation instruction document here to install FTC software.

## Slide 5: What is TRC Framework?
FTC SDK provides basic functionalities accessing hardware, communicating and controlling the robot.
TRC Library extends FTC SDK to provide even more functionalities and complex algorithms that are not game specific.
TRC Library is the core of our robot code. Its benefits include:
  Literally avoid re-inventing the wheel every season and allow us to focus on coding competition specific strategies.
  Library code has been tested extensively every season and therefore very stable.
  Provide a mechanism to pass on knowledge from one generation to the next allowing us to create increasingly complex robot strategies.

## Slide 6: TRC Framework Organization
TRC Framework architecture allows sharing between FTC and FRC: The layering approach.
  TrcCommonLib: Common code identical to both FTC and FRC (majority of the framework).
  TrcFtcLib: FTC specific libraries.
  TrcFrcLib: FRC specific libraries.
TRC Framework consists of the following categories:
  Input: Provides wrappers for input devices such as game controllers, Driver Station Dashboard and sensors (e.g. gyros, encoders, distance sensors, limit switches etc).
  Output: Provides wrappers for actuators such as motor controllers, servos, drive bases, indicators (e.g. SmartDashboard, LEDs) etc.
  Complex Control: Provides complex control algorithms such as PIDF Control and path following (e.g. PurePursuit) etc.
  Vision: Provides wrappers for communicating with cameras and various vision processing (e.g. AprilTag, OpenCV, TensorFlow).
  System: Provides system services such as multi-tasking support, protocol support for different buses (e.g. I2C, Serial), timers, events, utilities and diagnostics.

## Slide 7: FTC Template Project
TRC provides an FTCTemplate project on GitHub. https://github.com/trc492/FtcTemplate
The java template code is located in the folder TeamCode/src/main/java, within which contains several java packages:
  TrcCommonLib – contains code modules that are shared between FTC and FRC.
  TrcFtcLib - contains code modules that are specific to FTC.
  teamcode – contains the main competition code.

## Slide 8: Robot Code Organization
In the teamcode package, the provided code template folders/files are:
  autocommands folder – all autonomous strategy code are located here.
    CmdAuto.java – Template code for implementing an autonomous strategy.
  autotasks folder – all auto-assist task code are located here.
    TaskAuto.java – Template code for implementing an auto-assist task.
  drivebases folder – all Drive Base code are located here.
    RobotDrive.java – contains code that’s common to all types of drive bases.
    MecanumDrive.java – contains code implementing a mecanum drive base.
    SwerveDrive.java – contains code implementing a swerve drive base.
  subsystems folder – all Subsystem code are located here.
    BlinkinLEDs.java – contains code to manage an LED strip controlled by the REV Blinkin controller.
  vision folder – contains vision code.
  Robot.java – contains code to create and configure all robot hardware and subsystems.
  RobotParams.java – contains all robot preferences and configuration information.
  FtcAuto.java – contains code for the Autonomous OpMode.
  FtcTeleOp.java – contains code for the TeleOp OpMode.
  FtcTest.java – contains code for the Test OpMode.

## Slide 9: FTC Robot Modes
FTC match consists of two periods:
  30 seconds Autonomous period
  2 minutes TeleOp period (last 30 seconds is the end game)
The robot can be in one of the three modes:
  Autonomous mode – the robot is totally controlled by sensors and code without any human control.
  TeleOp mode – the robot is controlled by human players.
  Test mode – diagnostic, test or tuning code are generally run in this mode.
Each robot mode has its own OpMode program: FtcAuto.java, FtcTeleOp.java and FtcTest.java.
During an FTC match, the following sequence of events will happen:
  Driver selects the FtcAuto OpMode on the Driver Station and starts its initialization.
  Driver selects all the autonomous options with the choice menus.
  Driver starts the Autonomous period which lasts 30 seconds and the OpMode will automatically stop.
  Driver selects the FtcTeleOp OpMode on the Driver Station and starts its initialization.
  When the bell rings, driver starts the TeleOp period which lasts 2 minutes.
  When the bell rings, driver stops the TeleOp period which concludes a match.

## Slide 10: FTC OpModes: FtcAuto, FtcTeleOp, FtcTest
  All OpModes extends FtcOpMode which means they must implement the following methods:
    robotInit: contains code to create and configure all robot hardware and subsystems. This is called once when the “Init” button on the Driver Station is pressed.
    initPeriodic: contains code that will be called repeatedly after robotInit is called but before competition starts. This method is optional. If provided, it typically monitors sensor states (e.g. Vision to detect objects before Autonomous starts).
    startMode: contains code to initialize all subsystems to start a competition OpMode. This is called once when the “Play” button on the Driver Station is pressed.
    stopMode: contains code to stop/cleanup all subsystems to end a competition OpMode. This is called once when the “Stop” button on the Driver Station is pressed.
    periodic: contains code that will be called repeatedly after competition starts to perform competition tasks.

## Slide 11: OpMode Execution Flowchart
robotInit method is called once when the “Init” button is pressed.
initPeriodic method is called repeatedly until “Start” button is pressed.
startMode method is called once when “Start” button is pressed.
periodic method is called repeatedly until “Stop” button is pressed.
stopMode method is called once when “Stop” button is pressed.

## Slide 12: Robot.java
Java is an Object Oriented Programming language (OOP). It means everything are built upon objects organized in a hierarchical structure.
Robot provides the following methods:
  Constructor – contains code to create and configure all hardware and subsystems.
  robotStartMode – is called to do appropriate robot initialization before starting the OpMode.
  robotStopMode – is called to do appropriate robot cleanup before exiting the the OpMode.
  Miscellaneous methods to facilitate hardware/subsystem accesses.

## Slide 13: 2022-2023: Power Play Robot Organization

## Slide 14: RobotParams.java
RobotParams.java contains preferences and parameters of the robot and subsystems.
Preferences:
  Enable and disable hardware and subsystems: it is especially useful when debugging subsystems during development when some hardware may not exist yet.
  Robot and competition field characteristics: constants such as robot dimensions, field dimensions, robot starting locations, field element locations.
  Hardware/Subsystem parameters: specifies hardware/subsystem properties and parameters.