## Slide 1: Advanced Robotics Programming Class Lesson 8: Vision
Titan Robotics Club FTC3543
Michael Tsang (Programming Mentor)

## Slide 2: Agenda
In this lesson, you will learn all about vision:
  What is Vision Processing?
  Vision Info Processing
  OpenCV Pipeline
  OpenCV Vision
  OpenCV Color Blob Detection Pipeline
  OpenCV AprilTag Detection Pipeline
  PhotonVision
  Lime Light Vision

## Slide 3: What Is Vision Processing?
Using camera allows the robot to see things but seeing things means more than just capturing a picture. A picture is not very useful unless it is “interpreted” or “processed” by somebody to figure out what objects are in the picture and where they are relative to the camera.
Fortunately, there are object detection libraries such as OpenCV (Open Source Computer Vision). They can do vision processing on a picture and return useful info such as object types detected and object locations. Some libraries even provide “Machine Learning” tools that allow you to feed thousands of pictures to it so it can learn different type of objects. These are very advanced topics that we don’t have to deal with. In other words, they are generally provided to us in the form of library APIs or even camera firmware.
What we are learning here is how to use the processed vision info to navigate the robot.

## Slide 4: Vision Info Processing
Generally, for each picture frame it processed, vision returns an array of objects with the following info:
  The type of object detected.
  The rectangle of the detected object (includes the pixel coordinates of the center of the detected object and the size of the detected object rectangle).
  Optionally, the location of the object relative to the camera.
  Some vision processor may include confidence level.
Vision libraries: OpenCV and WPILib provide some amount of processing of the camera frames. On top of it, TRC library will process the returned info adding even more info. For example, if OpenCV or WPILib do not give us object location info, TRC library will translate pixel coordinates and size into real world units using Homography mapper giving us object location info (distance and angle) from the camera.
Our game specific processing:
  Apply filtering algorithm to eliminate false detection and hopefully we will have exactly one object in the array which is our target.
  If the array still contains more than one object, we will sort the array with a set of criteria so that the first object in the array should have the highest confidence.
With the object distance and angle info, one can create a PID controlled drive (TrcPidDrive) using the vision info of the detected object to control the Y axis travel and robot heading.

## Slide 5: OpenCV Pipeline
OpenCV is an open source industry standard vision processing library.
An OpenCV pipeline provides a method that takes a camera frame and runs it through a sequence of filters in order to isolate and find the object we wish to detect.
OpenCV library provides many different filters:
  Image processing: Blur, Desaturate, Distance transform, HSV threshold, HSL Threshold, RGB threshold, Resize, Normalize, Mask.
  Feature detection: Convex hulls, Filter contours, Find blobs, Find contours, Find lines, Watershed, Cascade classifier.
TRC library provides two generic software pipelines:
  Color blob detection pipeline.
  AprilTag detection pipeline.

## Slide 6: OpenCV Vision
Without vision coprocessors, TRC library supports OpenCV vision processing running OpenCV pipelines on the RoboRIO on a standalone thread.
Vision processing is CPU intensive and will impact the overall robot and vision performance. Therefore, we recommend using a vision coprocessor if possible.
TRC library provides two generic vision pipelines:
  Color blob detection: detects a blob with the specified color range.
  AprilTag detection: detects printed AprilTag images.

## Slide 7: OpenCV Color Blob Detection Pipeline
TRC library provides a generic color blob detection pipeline that does the following:
  Filter by color (HSV threshold, HSL threshold, RGB threshold).
  Find contours.
  Filter Contours (width, height, area, perimeter, solidity, vertex count, aspect ratio).
  Annotate frame.
Constructor: TrcOpenCvColorBlobPipeline(String instanceName, int colorConversion, double[] colorThresholds, FilterContourParams filterContourParams, TrcDbgTrace tracer)
  colorConversion: specifies color conversion before processing the image (e.g. Imgproc.BGR2HSV).
  colorThresholds: specifies the color ranges for the 3 colors (e.g RGB or HSV).
  filterContourParams: specifies the contour filtering criteria (e.g. width, height, aspect ratio etc).
Methods: void reset() DetectedObject[] getDetectedObjects()
FIRST provided a GRIP tool for building and tuning OpenCV pipelines, see documentation here.

## Slide 8: OpenCV AprilTag Detection Pipeline
TRC library provides an OpenCV AprilTag detection pipeline that detects AprilTag images.
Constructor: FrcOpenCvAprilTagPipeline(String tagFamily, AprilTagDetector.Config detectorConfig, AprilTagPoseEstimator.Config poseEstConfig, TrcDbgTrace tracer)
  tagFamily: specifies the AprilTag family to detect.
  detectorConfig: specifies the detector configuration (generally not specify to use default).
  poseEstConfig: specifies the pose estimator configuration (AprilTag size and camera characteristics).
Methods: void reset() DetectedObject[] getDetectedObjects()

## Slide 9: Photon Vision
TRC library provides another AprilTag detection using the FIRST provided Photon library.
Photon library is similar to our OpenCV AprilTag Pipeline and may arguably provide slightly better functionality with pose estimation.
Constructor: FrcPhotonVision(String cameraName, double camHeight, double camPitch, TrcDbgTrace tracer)
  cameraName: specifies the camera name.
  camHeight: specifies the camera mounting height off the ground.
  camPitch: specifies the camera mounting pitch from horizontal.
Methods: void cancel() boolean detectObjects(TrcEvent event, double timeout) boolean detectBestObject(TrcEvent event, double timeout) DetectedObject[] getDetectedObjects() DetectedObject getBestDetectedObject()

## Slide 10: Lime Light Vision
Lime Light is a vision coprocessor. It is a Raspberry PI running Linux Operating System with built-in software to process vision for the FRC season. FIRST provides the vision processing software for the season close to kickoff (for LimeLight and other Coprocessors).
Built-in vision software is based on OpenCV. LimeLight provides two types of vision processing pipeline:
  Color Blob detection: detects a blob with the specified color range.
  AprilTag detection: detects printed AprilTag images.
Since vision processing is running on the coprocessor, it does not impact robot performance and provides excellent detection frame rate.
Constructor: FrcLimeLightVision(String instanceName, TrcDbgTrace tracer)
Methods: DetectedObject getDetectedObject() int getSelectedPipeline() void selectPipeline(int pipeline)