## Slide 1: Advanced Robotics Programming Class Lesson 1: Introduction to Titan Robotics Framework
Titan Robotics Club FRC492
Michael Tsang (Programming Mentor)

## Slide 2: Advanced Robotics Programming Class
Titan is using Java as the programming language for both FTC and FRC.
We developed an extensive Java Robotics Framework shared between FTC and FRC.
This class focuses on learning how to use this framework.
Class material is focused on FRC robots but most of the class materials should still be applicable to FTC.
What this class doesn’t cover: We don’t teach Java language here. We assume you are proficient in writing Java code. If you need to learn Java, you need the Beginner Class or there are many on-line resources learning Java.
Notes: Make sure students are at the correct level (poll for Java knowledge)

## Slide 3: Agenda
In this lesson, we will learn about the Titan Robotics Framework:
  Software Installation
  TRC Framework Organization
  FRC Template Project
  FRC Robot Modes
  Robot Code Organization

## Slide 4: Software Installation
GitHub: That's where all our code repositories are stored. If you don't already have a GitHub account, register for one here. Our code repositories can be found here.
GitHub Desktop app: GUI application to manage GitHub repositories (download and install from here).
Install FRC software: Installation instructions can be found here. This installs the WPILib that includes Visual Studio Code which is the IDE to develop Java code for FRC.
Optionally, you can also install the FRC Game Tools here which contains FRC Driver Station and RoboRIO Imaging Tool.
Install 3rd Party Vendor Libraries: This is done inside Visual Studio Code. The instructions can be found here. There are many 3rd party libraries. We don't need all of them. The must haves are listed below. If we need more, we can install them later.
  CTRE Phoenix Toolsuite - for CTRE motor controllers such as Talons and Falcons.
  Kauai Labs - for NavX IMU.
  Rev Robotics SPARKMAX - for SparkMax motor controllers.
Finally, it is highly recommended you read the document here to familiarize yourself with how FRC software works. The software installation steps above is essentially a quick summary from reading this doc.

## Slide 5: What is TRC Framework?
WPILib provides basic functionalities accessing hardware, communicating and controlling the robot.
TRC Library extends WPILib to provide even more functionalities and complex algorithms that are not game specific.
TRC Library is the core of our robot code. Its benefits include:
  Literally avoid re-inventing the wheel every season and allow us to focus on coding competition specific strategies.
  Library code has been tested extensively every season and therefore very stable.
  Provide a mechanism to pass on knowledge from one generation to the next allowing us to create increasingly complex robot strategies.

## Slide 6: TRC Framework Organization
TRC Framework architecture allows sharing between FTC and FRC: The layering approach.
  TrcCommonLib: Common code identical to both FTC and FRC (majority of the framework).
  TrcFtcLib: FTC specific libraries.
  TrcFrcLib: FRC specific libraries.
TRC Framework consists of the following categories:
  Input: Provides wrappers for input devices such as joysticks, game controllers, Driver Station and sensors (e.g. gyros, encoders, distance sensors, limit switches etc).
  Output: Provides wrappers for actuators such as motor controllers, servos, pneumatics, drive bases, indicators (e.g. SmartDashboard, LEDs) etc.
  Complex Control: Provides complex control algorithms such as PIDF Control and path following (e.g. PurePursuit) etc.
  Vision: Provides wrappers for communicating with cameras and various vision processing (e.g. OpenCV, AprilTag).
  System: Provides system services such as multi-tasking support, protocol support for different buses (e.g. I2C, Serial), timers, events, utilities and diagnostics.

## Slide 7: FRC Template Project
TRC provides an FRCTemplate project on GitHub. https://github.com/trc492/FrcTemplate
The java template code is located in the folder src/main/java, within which contains several java packages:
  TrcCommonLib – contains code modules that are shared between FTC and FRC.
  TrcFrcLib - contains code modules that are specific to FRC.
  team492 – contains the main competition code.

## Slide 8: FRC Robot Modes
The robot can be in one of the four modes:
  Disabled mode – the robot is powered ON but not operational, generally safe to work on the robot.
  Autonomous mode – the robot is totally controlled by sensors and code without any human control.
  TeleOp mode – the robot is controlled by human players.
  Test mode – diagnostic, test or tuning code are generally run in this mode.
FRC match consists of two periods:
  15 seconds Autonomous period
  2 minutes 15 seconds TeleOp period
During an FRC match, the robot starts in Disabled mode and transitions between different modes. Disabled -> Autonomous -> Disabled -> TeleOp -> Disabled

## Slide 9: Robot Code Execution Flowchart
initRobot in Robot.java is called once when the program is loaded.
When starting Autonomous mode, there will be a mode change from Disabled mode to Autonomous mode.
stopMode in FrcDisabled.java and robotStopMode in Robot.java is called to exit Disabled mode.
robotStartMode in Robot.java and startMode in FrcAuto.java is called to enter Autonomous mode.
While in Autonomous mode, periodic in FrcAuto.java is called periodically in a loop.
When Autonomous period ended, there will be a mode change from Autonomous mode to Disabled mode.
stopMode in FrcAuto.java and robotStopMode in Robot.java is called to exit Autonomous mode.
robotStartMode in Robot.java and startMode in FrcDisabled.java is called to enter Disabled mode.
While in Disabled mode, periodic in FrcDisabled.java is called periodically in a loop.
When starting TeleOp period, there will be a mode change from Disabled mode to TeleOp mode.
stopMode in FrcDisabled.java and robotStopMode in Robot.java is called to exit Disabled mode.
robotStartMode in Robot.java and startMode in FrcTeleOp.java is called to enter TeleOp mode.
While in TeleOpmode, periodic in FrcTeleOp.java is called periodically in a loop.
When TeleOp period is ended, there will be a mode change from TeleOp mode to Disabled mode.
stopMode in FrcTeleOp.java and robotStopMode in Robot.java is called to exit TeleOp mode.
robotStartMode in Robot.java and startMode in FrcDisabled.java is called to enter Disabled mode.
While in Disabled mode, periodic in FrcDisabled.java is called periodically in a loop.

## Slide 10: Robot Code Organization
In the team492 package, the provided code template files are:
  Main.java – Entry point to the robot code and is provided by FIRST (do not modify)
  Robot.java – Extending FrcRobotBase which extends RobotBase provided by WPILib
  FrcDisabled.java – Implementing TrcRobot.RobotMode which contains code run in Disabled mode
  FrcAuto.java – Implementing TrcRobot.RobotMode which contains code run in Autonomous mode
  FrcTeleOp.java – Implementing TrcRobot.RobotMode which contains code run in TeleOp mode
  FrcTest.java – Implementing TrcRobot.RobotMode which contains code run in Test mode

## Slide 11: Robot.java
Java is an Object Oriented Programming language (OOP). It means everything are built upon objects organized in a hierarchical structure.
Robot is the top level container. It contains all subsystems and is the entry point to our robot code.
Robot extends FrcRobotBase which means it must implement the required abstract methods:
  robotInit – is called once when the robot code is loaded and contains code to create and initialize robot components and subsystems.
  robotStartMode – is called during mode transition to a new mode and contains code to do appropriate robot initialization before starting the new mode.
  robotStopMode – is called during mode transition out of a previous mode and contains code to do appropriate robot cleanup before exiting the previous mode.

## Slide 12: 2022-2023: Charged Up Robot Organization

## Slide 13: FrcDisabled, FrcAuto, FrcTeleOp and FrcTest
All these modules implement TrcRobot.RobotMode which means it must implement the following methods:
  startMode – is called before starting the corresponding robot mode and contains code to initialize/enable components necessary for the robot mode.
  stopMode – is called before exiting the corresponding robot mode and contains code to cleanup/disable components necessary for the robot mode.
  periodic – is called periodically during the robot mode to perform various low frequency tasks such as reading human input or displaying status or high frequency tasks such as PID controlled drive or autonomous state machines.