## Slide 1: Advanced Robotics Programming Class Lesson 7: Autonomous
Titan Robotics Club FRC492
Michael Tsang (Programming Mentor)

## Slide 2: Agenda
In this lesson, you will learn everything about Autonomous:
  Autonomous Nomenclature.
    Operation
    RobotCommand
    AutoTask
  What is an autonomous program?
  Steamworks Autonomous Analyzed
  Timer
  Shuffleboard
  FrcDashboard
  FrcChoiceMenu

## Slide 3: Autonomous Nomenclature
Before we dive into autonomous, let’s define some of the terms we will be using:
  Operation: An operation usually takes time, it has a start, in-progress and an end. To perform an operation, we start the operation, wait for the progress until it is finished.
  RobotCommand: An autonomous program that performs a sequence of operations using a state machine. Some operations can be started in parallel in the same state (don’t have dependencies to each other), others may need to wait for the previous operation(s) to finish before starting in a separate state. RobotCommand must be run by periodically calling its cmdPeriodic method usually by the main robot thread.
  AutoTask: A sub-command that performs a sequence of operations that can be called by another RobotCommand or TeleOp code as an auto-assist operation. An AutoTask is an asynchronous operation (i.e. call to start, signal event when finished) and runs in your specified task.

## Slide 4: Operation
In TRC library, all operations that take time to finish are asynchronous. Calling them will start the operations but control will return immediately. It means the actual work is done on a separate periodic task. To allow synchronization, an asynchronous operation accepts either an event or a callback to notify when an operation is completed.
Examples of asynchronous operations in the TRC library:
  motor.set(double delay, double value, double duration, TrcEvent event)
  motor.setPosition(double delay, double pos, boolean holdTarget, double powerLimit, TrcEvent event, double timeout)
  pidDrive.setRelativeTarget(double xDelta, double yDelta, double turnDelta, boolean holdTarget, TrcEvent event, double timeout)
  purePursuitDrive.start(TrcEvent event, TrcPose2D startingPose, boolean incrementalPath, TrcPose2D... poses)

## Slide 5: RobotCommand
RobotCommand usually implements a state machine with a number of states. Each state contains code to perform a number of independent operations that don’t depend on each other. Then it will wait for one or more of these operations to finish via events before moving onto the next state.
RobotCommand must provide the following methods:
  boolean cmdPeriodic(double elapsedTime): called periodically to execute the RobotCommand usually by Autonomous using the main robot thread.
  boolean isActive(): check if the RobotCommand is still in progress.
  void cancel(): call to cancel the RobotCommand.
State machine methods commonly used in RobotCommand:
  T checkReadyAndGetState(): check if the state machine is in ready state and get its state.
  void setState(T state): set and transition the state machine to the specified state.
  void waitForSingleEvent(TrcEvent event, T nextState): wait for an event and then transition to the specified next state.
  void waitForEvents(T nextState, boolean waitForAllEvents): wait for multiple events and then transition to the specified next state.
  void addEvent(TrcEvent event): add events before calling waitForEvents.

## Slide 6: AutoTask
AutoTask implements a sub-command using state machine and can be called by RobotCommand or TeleOp as an auto-assist operation.
AutoTask can be viewed as an asynchronous operation that performs the operations on a specified task.
AutoTask Constructor: TrcAutoTask(String instanceName, String owner, TrcTaskMgr.TaskType taskType, TrcDbgTrace msgTracer)
Methods provided:
  void startAutoTask(T startState, Object taskParams, TrcEvent completionEvent): start the auto task with the specified start state and task parameters, can optional specify an event to signal when auto task is completed.
  void stopAutoTask(boolean completed): stop the auto task and specify whether the task was completed or canceled.
  boolean isActive(): check if the auto task is still in progress.
Must implement the following methods:
  boolean acquireSubsystemsOwnership(): add code to acquire ownership of subsystems involved in the auto task.
  void releaseSubsystemsOwnership(): add code to release ownership of subsystems acquired.
  void stopSubsystems(): add code to stop all subsystems involved.
  void runTaskState(Object params, T state, TrcTaskMgr.TaskType taskType, TrcRobot.RunMode runMode, boolean slowPeriodicLoop): add code to implement the state machine to execute the operations.

## Slide 7: What is an Autonomous Program?
Autonomous program is an RobotCommand runs on the main robot thread. It consists of a sequence of steps (i.e. states) to be performed by the state machine using various sensors as input and actuators as output without any human control.
The easiest way to design an autonomous program is to break down the task into steps in English. Each step consists of operations that can be performed in parallel and therefore can be started in the same state of the task. Operation that depends on previous operations must be started in a new state and will not start until the operations in the previous state are finished by which time the task will transition to this new state.
Let’s look at the autonomous period of the 2017 FIRST Steamworks season. 2017 FIRST Robotics Competition STEAMWORKS Game Animation – YouTube
Three ways to score in autonomous:
  Cross the baseline (5 pts).
  Score fuel in the boiler (1 pt per fuel into the top goal and 1 pt per 3 fuels into the bottom goal).
  Deliver gear to the airship (60 pts per rotor turning).
Autonomous period is only 15 seconds long, so we need to pick our strategy on what we can accomplish.
Here is a video of how we did in autonomous in one of the matches. First Steamworks: Galileo Semifinal 1 Match 1 (World Championship - Houston) - YouTube

## Slide 8: Steamworks Autonomous Analyzed
First, we set our autonomous goals trying to maximize our score within the 15-second period:
  Cross the baseline.
  Deliver the gear to the airship.
  Run as far as we could to our gear loading station on the opponent side and stop.
Then, we layout the sequence of operations in English:
  Park the robot either on the left or the right side.
  Move forward 85 inches crossing the baseline.
  Turn left or right approx. 60 degrees toward the airship.
  Use vision to align with target.
  Move forward until about 7 inches in front of the peg.
  Deploy the gear onto the peg.
  Backup 36 inches.
  Turn back facing the opponent side.
  Move forward about 320 inches into the neutral zone.
  Stop.

## Slide 9: Exercise: Steamworks Autonomous
Create an autonomous command module for FIRST Steamworks that does the following:
  In previous exercises, you have already created a mecanum drive base.
  In Robot.java, add code to robotInit to create a pneumatic gear deployer (FrcPneumatics).
  Create a CmdAutoSteamWorksLeft.java implementing TrcRobot.RobotCommand passing Robot to its constructor.
  In its constructor, add code to create a state machine and an event.
  Add implementation for methods: isActive, cancel and cmdPeriodic.
  In cmdPeriodic, implement code for the state machine with the following operations:
    Go forward 7 feet.
    Turn right 60 degrees.
    Go forward 3 feet.
    Deploy the gear using pneumatics.
    Back up 3 feet.
    Turn back to face forward.
    Go forward 26 feet.
    Stop
  In FrcAuto.java, add a new Strategy AUTO_STEAMWORKS_LEFT.
  In FrcAuto.java, add code to startMode method to create CmdAutoSteamWorksLeft.

## Slide 10: Timer
From time to time, the robot needs a timing mechanism, waiting for a given period of time to past.
TrcTimer Constructor: TrcTimer(String instanceName)
Methods:
  void set(double time, TrcEvent event) – starts a timer that will signal an event when the specified time has expired.
  void set(double time, TrcEvent.Callback callback, Object callbackContext) – starts a timer that will call the specified callback method when the specified time has expired.
  void cancel() – cancels an active timer.
  boolean hasExpired() – checks if the timer has expired.
  boolean isCanceled() – checks if the timer was canceled.
  boolean isActive() – checks if the timer is still active (not expired and not canceled).

## Slide 11: Exercise: Timer
In previous exercise, you have created a SteamWorks autonomous. Add a timer as the first state of the state machine to optionally delay 5 seconds before starting the autonomous routine.
In CmdAutoSteamWorksLeft.java, add a delay argument to its constructor .
In the constructor, also add code to create a timer.
In CmdAutoSteamWorksLeft.java, add a new START state to the state machine in cmdPeriodic that checks if the delay argument was zero. If so, set the state to start the autonomous, otherwise, start the timer for the specified delay time and start the autonomous after delay has expired.
In FrcAuto.java, change the code in startMode to pass a 5 second argument when creating CmdAutoSteamWorksLeft.

## Slide 12: Shuffleboard
On Shuffleboard, you can create multiple tabs that group different controls on each tab. Typically, we have the following tabs:
  FMSInfo: This contains information transmitted to us by Field Management System such as event name, match type, match number, alliance color, driver station number and optionally game specific messages.
  Dashboard: This provides a 16-line display simulating an LCD panel. It can be used to show robot status or for debugging.
  Autonomous: User can enter parameters to control how autonomous behaves. For example, letting autonomous know the robot’s starting position, selecting the autonomous strategy and entering strategy specific parameters.
  Test: This contains test mode parameters such as selecting diagnostic tests and tuning parameters.
  Camera: This shows camera feeds.
  Graphs: This shows data graphs of sensors you may want to record.

## Slide 13: FrcDashboard
FrcDashboard communicates with the Driver Station dashboard app (e.g. Shuffleboard) via Network table in the form of key/data pairs where key is the string name associated with the data.
You can read from or write to the data associated with the key in the Network table.
On Shuffleboard, you can create a display field associated with a Network table entry. The display field can be a text field where it can display numbers and strings. It can also be a slider, a switch or a graph. The values on some of these field can be modified by the user in which case the robot can read values from them as input parameters.
Output methods:
  displayPrintf – Displays information on the 16-line “LCD panel”.
  clearDisplay – Clears the display panel.
  putNumber – Stores a number associated with the given key.
  putString – Stores a string associated with the given key.
  putBoolean – Stores a Boolean state associated with the given key.
  putData – Stores a data object associated with the given key.
Input methods.
  getNumber – get a number associated with the given key.
  getString- get a string associated with the given key.
  getBoolean – get a Boolean state associated with the given key.
  getData – get a data object associated with the given key.

## Slide 14: FrcChoiceMenu
FrcChoiceMenu is used to present choices to the drivers to select match options on the Driver Station. It creates a SendableChooser to be sent to the dashboard that can be interpreted by Shuffleboard as a drop down menu with choices.
Constructor: FrcChoiceMenu(String menuTitle)
Methods:
  addChoice – Adds a choice to the choice menu.
  getCurrentChoiceObject – Gets the current choice data object.
  getCurrentChoiceText – Gets the current choice text.
  getTitle – Gets the menu title

## Slide 15: Exercise: Add SteamWorks to Auto Strategies
Add SteamWorks auto as one of the AutoChoices, connect the startDelay in AutoChoices to the delay argument in CmdAutoSteamWorksLeft and add a new field neutralZoneDistance in AutoChoices.
  In FrcAuto.java, add code to the AutoChoices constructor to add the new AUTO_STEAMWORKS_LEFT choice.
  Change code in startMode to pass startDelay as the delay argument in the construction of CmdAutoStreamWorksLeft.
  Add a new String field variable DBKEY_AUTO_NEUTRAL_ZONE_DISTANCE and set it to “Auto/NeutralZoneDistance”.
  Add code to the AutoChoices constructor to add the new number field named DBKEY_AUTO_NEUTRAL_ZONE_DISTANCE with a default value of 312 inches (Hint: userChoices.addNumber).
  Add a new method getNeutralZoneDistance to the AutoChoices class returning the value of the field.
  In CmdAutoSteamWorksLeft.java, add a new argument neutralZoneDistance in its constructor.
  Change code in cmdPeriodic to use the new neutralZoneDistance argument to navigate the robot out to the neutral zone.
  In FrcAuto.java, change code in startMode to add the neutralZoneDistance from AutoChoices as the new argument when constructing CmdAutoSteamWorksLeft.

## Slide 16: Exercise: ChargedUp AutoAssistScoreCube
Create an AutoTask that performs the auto-assist scoring of a cube.
  In previous exercises, you have already created a mecanum drive base and an elevator.
  In Robot.java, add code in robotInit to create an arm with gravity compensation (TrcPidActuator) and an intake (FrcCANTalon) that has a motor to spit the cube out (depositing it to score).
  Create a TaskAutoScore.java extending TrcAutoTask passing owner name string and Robot to its constructor.
  In its constructor, add code to create events for various operations.
  Add a method autoAssistScoreCube passing a completion event as its argument.
  Add a method autoAssistCancel with no argument.
  Add implementation for the acquireSubsystemsOwnership, releaseSubsystemsOwnership, stopSubsystems and runTaskState methods.
  In the runTaskState method, implement code for the state machine with the following operations:
    Raise the elevator to scoring height.
    Raise arm to scoring position.
    Score the cube by dropping it from the intake.
    Retract elevator.
    Retract arm.
    Back up 2 feet.
    Stop.