## Slide 1: Advanced Robotics Programming Class Lesson 4: Robot Subsystems
Titan Robotics Club FRC492
Michael Tsang (Programming Mentor)

## Slide 2: Agenda
In this lesson, you will learn to create complex robot subsystems.
  Drive Bases:
    Simple Drive
    Mecanum Drive
    Swerve Drive.
  Passive Wheel Odometry.
  PID controlled position actuators: Elevator, Arm, Wrist and Turrets (TrcPidActuator).
  PID controlled conveyors (TrcPidConveyor).

## Slide 3: Simple Drive Base
Simple drive base consists of 4 to 6 wheels (most likely 6 wheels) using tank drive strategy, does not support holonomic drive. Usually very hard to turn and therefore we use West Coast Drive configuration with 6 wheels where middle wheels are slightly lowered.
Usually have 4 motors (2 left and 2 right). The middle and back wheels are usually mechanically linked and driven by one motor. The front has its own motor.
Each side has an encoder. Combining the left and right encoder values and a gyro to keep track of the drive base odometry (X, Y location on the field and robot orientation).
Pros: Not easy to push around.
Cons: Not very agile. If robot is not aligned with target, need to back up, turn and go forward again.
Constructors: TrcSimpleDriveBase(TrcMotor leftMotor, TrcMotor rightMotor, TrcGyro gyro)
Methods: boolean supportsHolonomicDrive() void stop() void tankDrive(double leftPower, double rightPower) void arcadeDrive(double drivePower, double turnPower)

## Slide 4: Mecanum Drive Base
TrcMecanumDriveBase extends TrcSimpleDriveBase and consists of 4 wheels using holonomic drive strategy. It allows the robot to move forward/backward/turn and strafe (sideway).
Ha 4 motors (left front, right front, left back, right back). Each wheel has its own motor and encoder. By changing the spin direction of the diagonal wheels, it allows the robot to move sideways. Combining the four encoders and a gyro to keep track of the drive base odometry (X, Y location on the field and robot orientation).
Pros: Very agile, can move in any direction independent of the robot heading.
Cons: Can be pushed around easily. Strafing not very precise due to wheel slippage.
Constructors: TrcMecanumDriveBase(TrcMotor lfMotor, TrcMotor lbMotor, TrcMotor rfMotor, TrcMotor rbMotor, TrcGyro gyro)
Methods: boolean supportsHolonomicDrive() void stop() void holonomicDrive(double x, double y, double rotation)

## Slide 5: Swerve Drive Base
TrcSwerveDriveBase extends TrcSimpleDriveBase and consists of 4 swerve modules (left front, right front, left back, right back) using holonomic drive strategy. It allows the robot to move forward/backward/turn and strafe (sideway).
A swerve module has a drive motor and drive encoder. In addition, it has a steer motor and steer encoder. It allows the robot to move in any direction independent of the robot heading. Combining the four drive encoders and a gyro to keep track of the drive base odometry (X, Y location on the field and robot orientation).
Pros: Very agile, can move in any direction independent of the robot heading, not easily pushed around.
Cons: Very expensive, heavy.
Constructors: TrcSwerveDriveBase(TrcSwerveModule lfModule, TrcSwerveModule lbModule, TrcSwerveModule rfModule, TrcSwerveModule rbModule, TrcGyro gyro, double wheelBaseWidth, double wheelBaseLength)
Methods: boolean supportsHolonomicDrive() void stop() void holonomicDrive(double x, double y, double rotation) void setAntiDefenseEnabled(String owner, boolean enabled) boolean isAntiDefenseEnabled()

## Slide 6: Exercise: Mecanum Drive Base
In Robot.java, create four motor controllers named lfWheel, rfWheel, lbWheel and rbWheel with CAN ID 3, 4, 5 and 6 respectively (FrcCANTalon).
Invert the right wheel motors: setInverted(true).
Create a gyro (FrcAHRSGyro) specifying a name and the port SPI.Port.kMXP it is attached to.
Create the mecanum drive base (TrcMecanumDriveBase) specifying the four motors and the gyro.
In FrcTeleOp.java, add code in the periodic method to read the X and Y axes of the Xbox controller left stick for controlling the X and Y movement of the robot base. Read the X axis of the Xbox controller right stick for controlling the turn of the robot base.
Call the holonomicDrive method of the mecanum drive base specifying X, Y and rotation values from the game controller.
Print a message on the dashboard showing the X, Y and rotation power.

## Slide 7: Passive-wheel Odometry
The drive bases (simple, mecanum, swerve) created by the TRC library has built-in odometry that uses the encoders of the wheel motors and a gyro. The built-in odometry works fine as long as the wheels don’t slip.
If any of the driving wheels slipped or the robot hits the wall or being hit by another robot, the robot displacement may not be registered by the built-in odometry. This means the odometry is no longer accurate.
One solution to this problem is to use external passive-wheel odometry. A passive-wheel odometry sensor is built with passive omni-wheels with an encoder. It has no motor but if the wheel turns, the encoder will register rotation. If we put two passive-wheel odometry sensors one for each axis and spring loaded them to the ground, they will keep track of movements on both axes accurately even if the robot wheels slipped or the robot being pushed by other robots.

## Slide 8: TrcDriveBaseOdometry Class
TrcDriveBaseOdometry class provides external odometry device support for the drive base. It supports 5 different configurations:
  2-sensor configuration: one Y-axis encoder sensor and one gyro rotation sensor (for non-holonomic drive bases).
  3-sensor configuration 1: one X-axis encoder sensor, one Y-axis encoder sensor and one gyro rotation sensor.
  3-sensor configuration 2: two Y-axis encoder sensors and one gyro rotation sensor (for non-holonomic drive bases).
  4-sensor configuration: one X-axis encoder sensor, two Y-axis encoder sensors and one gyro rotation sensor (most common configuration).
  5-sensor configuration: two X-axis encoder sensor, two Y-axis encoder sensors and one gyro rotation sensor.
X/Y axis encoders must be installed parallel to the respective axis and tangential to the centroid of the drive base.
X/Y axis encoders can be installed with an offset from the centroid of the drive base.
For X-axis, the offset of the front sensor must be zero or positive, the offset of the back sensor must be zero or negative.
For Y-axis, the offset of the left sensor must be zero or positive, the offset of the right sensor must be zero or negative.

## Slide 9: TrcDriveBaseOdometry Class (continue)
TrcDriveBaseOdometry Constructor: TrcDriveBaseOdometry(AxisSensor[] xSensors, AxisSensor[] ySensors, TrcOdometrySensor angleSensor)
Methods:
  setOdometryScales – set X, Y and rotation scale factors (scaling sensor units into real world units).
  resetOdometry – reset odometry with options to reset the sensor hardware and rotation sensor.
  getOdometryDelta – reads all sensors and calculate the delta displacements of all axes from the last odometry update, called periodically by the drive base class to integrate delta displacements into absolute field position.

## Slide 10: PID Controlled Position Actuators
PID controlled actuator consists of a motor, a position sensor for feedback and optionally one or two limit switches. It applies PIDF to control the actuator to go to a certain position.
Supported features:
  Zero calibration.
  Stall detection/protection.
  Hardware/Software range limits.
  Position scale and offset.
  Position presets.
  Power compensation.
  Set and hold a position.
  TeleOp control of the actuator that understands range limits and will slow down when approaching limits (setPower, setPidPower).
Constructors: TrcPidActuator(String instanceName, TrcMotor motor, TrcDigitalInput lowerLimitSwitch, TrcDigitalInput upperLimitSwitch, Parameters params)
Useful methods: void setPower(double power) void setPidPower(double power) void setTarget(double target, boolean holdTarget) void setPresetPosition(int preset) void presetPositionUp() void presetPositionDown()

## Slide 11: Exercise: PID Controlled Elevator
In Robot.java, add code in robotInit method to create a TrcPidActuator.Parameters object and initialize it with proper parameters.
Create a motor, a lower limit switch, an upper limit switch and an elevator (FrcCANTalon, FrcDigitalInput, TrcPidActuator).
In FrcTeleOp.java, add code to the startMode method to zero calibrate the elevator.
Add code in the driverControllerButtonEvent method and assign the left bumper as the manual override (i.e. create a class variable manualOverride and set it to true if left bumper is pressed, false when the button is released).
Add code in the periodic method to read the Y axis of the Xbox controller right stick as the elevator power. If in manualOverride mode, call elevator.setPower with the joystick value. Otherwise, call elevator.setPidPower with the joystick value.
Add code to print the elevator power, elevator position as well as the states of the lower and upper limit switches.
Extra credit: hook up a power compensation handler to compensate for gravity (Hint: actuatorParams.setPowerCompensation).

## Slide 12: PID Controlled Conveyor
PID controlled conveyor consists of a motor, a position sensor for feedback, optionally an entrance sensor and an exit sensor. It applies PIDF to control the conveyor to move a certain distance.
Supported features:
  Distance scale.
  Unit object distance.
  Conveyor power (i.e conveyor speed).
  Conveyor capacity.
Constructors: TrcPidConveyor(String instanceName, TrcMotor motor, TrcDigitalInput entranceSensor, TrcDigitalInput exitSensor, Parameters params)
Useful methods: int getNumObjects() void setPreloadedObjects(int num) void registerEntranceEvent(TrcEvent event) void registerExitEvent(TrcEvent event) boolean isEntranceSensorActive() boolean isExitSensorActive() void move(int units) void advance() void backup()

## Slide 13: Exercise: PID Controlled Conveyor
In Robot.java, add code in robotInit method to create a TrcPidConveyor.Parameters object and initialize it with proper parameters.
Create a motor, an entrance sensor, an exit sensor and a conveyor (FrcCANTalon, FrcDigitalInput, TrcPidConveyor).
Add code in the driverControllerButtonEvent method to move the conveyor forward on button B and backward on button X and print a message on the dashboard reporting the button event (Hint: advance and backup).