## Slide 1: Advanced Robotics Programming Class Lesson 7: Misc
Titan Robotics Club FRC492
Michael Tsang (Programming Mentor)

## Slide 2: Agenda
In this lesson, you will learn …
  Blinkin?
  Timer
  Dashboard, ChoiceMenu
  Vision

## Slide 3: Input/Output on the Driver Station
HalDashboard can be used to display information on the Driver Station.
  Constructor: No need to instantiate it because HalDashboard always exists when the robot program is loaded. Just need to call HalDashboard.getInstance().
  Methods:
    displayPrintf – Displays information on the “display panel” of lines.
    clearDisplay – Clears the display panel.
    putNumber – Stores a number associated with the given key.
    putString – Stores a string associated with the given key.
    putBoolean – Stores a Boolean state associated with the given key.
    putData – Stores a data object associated with the given key.
    get* - get data associated with the given key from the Driver Station.
FrcChoiceMenu is used to present choices to the drivers to select match options on the Driver Station.
  Constructor: menu title.
  Methods:
    addChoice – Adds a choice to the choice menu.
    getCurrentChoiceObject – Gets the current choice data object.
    getCurrentChoiceText – Gets the current choice text.
    getTitle – Gets the menu title

## Slide 4: Exercise 6: Create a Choice Menu for Robot Movements
Similar to the exercise in robot drive base where we drive the robot forward/backward/strafe/turn using PID control but instead of using joystick buttons, we use choice menu.
  Create and configure 4 motors for a mecanum drive base.
  Create and configure an IMU (i.e. gyro among other things).
  Create and configure a mecanum drive base.
  Create and configure 3 PID controllers.
  Create and configure a PID Drive object with the drive base and 3 PID controllers.
  Create and configure a choice menu with 4 choices: drive forward 10 feet, strafe left 5 feet, drive backward 7 feet, turn left 90 degrees.
  Add code in TeleOp to read the choice entered and execute the action chose.

## Slide 5: What Is Vision Processing?
Using camera allows the robot to see things but seeing things means more than just capturing a picture. A picture is not very useful unless it is “interpreter” or “processed” by somebody to figure out what objects are in the picture and where they are relative to the camera.
Fortunately, there are object detection libraries such as OpenCV (Open Source Computer Vision). They can do vision processing on a picture and return useful info such as object types detected and object locations. Some libraries even provide “Machine Learning” tools that allow you to feed thousands of pictures to it so it can learn different type of objects. These are very advanced topics that we don’t have to deal with. In other words, they are generally provided to us in the form of library APIs or even camera firmware.
What we are discussing here is how to use the processed vision info to navigate the robot.

## Slide 6: Vision Info Processing
Generally, for each picture frame it processed, vision returns an array of objects with the following info:
  The type of object detected.
  The rectangle of the detected object (includes the pixel coordinates of the center of the detected object and the size of the detected object).
  Some vision processor may include confidence level.
Our processing:
  Apply filtering algorithm to eliminate false detection and hopefully we will have exactly one object in the array which is our target.
  If the array still contains more than one object, the objects in the array should be sorted with highest confidence first so we will just pick the first object on the list.
  Translate the pixel coordinates and size into real world units (TrcHomographyMapper). This includes the distance of the object from the robot and the angle alignment of the object relative to the robot’s heading.
With the object distance and angle info, one can create a PID controlled drive (TrcPidDrive) using the vision info of the detected object to control the Y axis travel and robot heading.

## Slide 7: Timer
From time to time, the robot needs a timing mechanism, waiting for a given period of time to past.
TrcTimer Constructor: TrcTimer(String instanceName)
Methods:
  void set(double time, TrcEvent event) – starts a timer that will signal an event when the specified time has expired.
  void set(double time, TrcEvent.Callback callback, Object callbackContext) – starts a timer that will call the specified callback method when the specified time has expired.
  void cancel() – cancels an active timer.
  boolean hasExpired() – checks if the timer has expired.
  boolean isCanceled() – checks if the timer was canceled.
  boolean isActive() – checks if the timer is still active (not expired and not canceled).